## Slide 1: CS 168 Addressing
Fall 2016
Scott Shenker
CS168.io
http://inst.eecs.berkeley.edu/~cs168/fa16/

## Slide 2
Ssssshhhhhhhhhhhhhhh

## Slide 3: Administrivia
Homework 1 due tomorrow at 5pm
Are you in E16A?
  If you do not contact me ASAP, I will expect you to take the 168 midterm in class
Extra office hours tonight at 8pm (420 Soda)
  Focused on homework
  No office hours right after class…..

## Slide 4: Story of my home network
Spanning trees are useful….

## Slide 5: Story of this lecture….
Let’s see how it goes..

## Slide 6: Fundamentals of Addressing

## Slide 7: Have covered everything but addresses!
4-bit
Version
4-bit
Header
Length
8-bit
Type of Service
(TOS)
16-bit Total Length (Bytes)
16-bit Identification
3-bit
Flags
13-bit Fragment Offset
8-bit Time to
Live (TTL)
8-bit Protocol
16-bit Header Checksum
32-bit Source IP Address
32-bit Destination IP Address
Options (if any)
Payload

## Slide 8: Current IP Addressing
Reflects series of necessary hacks
  Necessary to survive, but not pretty…
No one would design such a system from scratch
But before walking through the shame that is today’s IP addressing, we first try to design it from scratch….

## Slide 9: Use of Addresses
Used by routers to forward packets to destination
  Functions as “locator”
  You can use this to forward packets to destination
Sometimes also used as identifier (subtle)
  Must let destination know packet was for them
    I know what my address is
  Might let destination know who packet is from
    This address tells me who you are (not typical)
Typically addresses are mostly locators
  Contains information about how to reach host

## Slide 10: Forwarding vs Routing
Routing: “control plane”
  Computing paths the packets will follow
  Distributed protocol leads to state at each router
  Can be done slowly (tens of milliseconds)
  But must scale to size of network!
Forwarding: “data plane”
  Directing a data packet to an outgoing link
  Individual router using routing state
  Must be done quickly (micro or nano seconds)

## Slide 11: Two Requirements for Addressing
Scalable routing
  How much state must be exchanged to create paths
  Some addressing schemes require more than others
Efficient forwarding
  How big is the forwarding table?
  How quickly can you locate items in table?

## Slide 12: One Additional Requirement
Host must be able to recognize packet is for them
  They should be able to tell that sender meant for that packet to reach them
This is a subtle issue….but important
  Think of this as the end-to-end check on routing!

## Slide 13: Recognizing Packets are for Me
Address can contain something intrinsic to me
  Functions somewhat as identifier
I know my current address
  Can recognize that incoming packet is using that address
Layers handle this differently:
  L2 addresses are “intrinsic”
  L3 addresses are assigned (and ephemeral)

## Slide 14: Layer 2 Addressing
Typically uses MAC addresses
Unique numbers burned into interface cards
  Random string of bits
  No location information
Local area networks route on these “flat” addresses
  Separate routing entry for each host
Works nicely with learning switches and STP
  Routes set up “on-demand”

## Slide 15: How Does This Meet Requirements?
Scalable routing
  Routing is done by learning switches
  Can scale to size of L2 networks
Efficient forwarding
  Exact match lookup on MAC addresses
  Only need table for “active” hosts
Host must be able to recognize packet is for them
  MAC address does this perfectly
Conclusion: scaling limited by table size (# hosts)

## Slide 16: How Would You Scale L2?
If your L2 network were too big to have separate entries for every host, how would you scale it?
Must use MAC address as part of address
  Only way host knows that the packet is for them
But how do you avoid having separate routing entries (in switches) for every host?

## Slide 17: DIY Scalable L2 Routing/Addressing
Take five minutes
Talk to your neighbors
Requirement for solution:
  Scales to large networks
  Internal switch routing tables relatively small and stable
    Not updated for every host movement
    No separate entry for every host
  But first-hop switch might have other information based on learning or other protocol

## Slide 18: Solution
Run standard routing algorithm between switches
  Internal routing tables know how to reach switches
  Don’t know anything about hosts
When host sends packet
  First-hop router adds tag to destination address
    Which switch should this be delivered to (if not known, flood)
  First-hop router adds tag to source address
    Telling everyone that this host is located at this switch
All internal forwarding done on switch address
  Smaller number, very stable
  But last switch delivers to individual host

## Slide 19: Addressing
Addresses are of form: Switch : Host
All internal forwarding done on switch addresses
  Fewer in number (than hosts)
  Very stable
Mapping between hosts and switches
  Learned as in normal L2 (or some other mechanism)
  Information only kept at edge
Hosts know that packet is for them (MAC address)
  Don’t need to know which switch they are at

## Slide 20: Status
Several protocols (SPB, Trill) are adopting this approach
Driven mainly by need to avoid spanning tree, not size of routing tables

## Slide 21: How Do We Extend This to L3?
Must extend to entire world!
Routing tables cannot have entry for every switch
Cannot use learning to know where hosts are

## Slide 22: DIY Scalable L3 Routing/Addressing
Take three minutes
Talk to your neighbors
Requirement for solution:
  Scales to global networks

## Slide 23: One Solution
Use addresses of the form: Network : Host
Routers know how to reach all networks in world
  Routers ignore Host part of address
  Hosts can recognize when packets are for them (Host)
Each network knows how to reach hosts
  E.g., using L2
A lookup mechanism allows hosts to know where every host is (i.e., which network to send to)
This was the original IP addressing scheme

## Slide 24: Two Key Aspects of Solutions
Aggregation
Mapping between identifier and locator

## Slide 25: Aggregation
Aggregation: Single forwarding entry used for many individual hosts
Examples:
  Scaled L2: Aggregate was “switch”
  L3: Aggregate was “network”
Advantages: fewer entries and more stable
  Don’t need to keep state on individual hosts
  Aggregate doesn’t move around much

## Slide 26: Name/Identifier to Location Mapping
Scaled L2: used learning to map host to switch
L3: uses DNS (not yet covered)
  Use “name” as identifier
  Get back IP address as locator

## Slide 27: Where Are We?
Have a sensible addressing scheme for scaling L2
  Use MAC addresses for host addressing
  But forward based on destination switch addresses
We have a sensible addressing scheme for L3
  Use Network:Host addressing
  Routers Forward on Network field

## Slide 28: How Do These Fit Together?
When sending packet from A to B….
A sends over L2 network to router
  Using MAC address of router and L2 forwarding
Series of routers carry packets to B’s L2 network
  Looking at network portion of IP address
B’s L2 network delivers packet to B
  Using B’s MAC address and L2 forwarding
  How do you find out about B’s MAC address?
    ARP (to be covered later)

## Slide 29: Hierarchical Structure
The Internet is an “inter-network”
  Used to connect networks together, not hosts
Forms a natural two-level hierarchy:
  WAN delivers to the right LAN
  LAN delivers to the right host
host
host
host
LAN 1
...
host
host
host
LAN 2
...
router
router
router
WAN
WAN
LAN = Local Area Network (L2)
WAN = Wide Area Network (L3)

## Slide 30: Two Universal Tricks in CS
When you need more flexibility, you add…
  A layer of indirection
When you need more scalability, you impose…
  A hierarchical structure

## Slide 31: Hierarchical Addressing in U.S. Mail
Addressing in the U.S. mail
  Zip code: 94704
  Street: Center Street
  Building on street: 1947
  Location in building: Suite 600
  Name of occupant: Scott Shenker
Forwarding the U.S. mail
  Deliver letter to the post office in the zip code
  Assign letter to mailperson covering the street
  Drop letter into mailbox for the building/room
  Give letter to the appropriate person
???

## Slide 32: Quick Review
Original IP addressing: Network : Host
Elegant, but perhaps not sufficiently scalable

## Slide 33: Extending The L3 Solution
If too many networks, then could add layer:
AS : Network : Host
AS = Autonomous System (often your ISP)
Network might be L2 network within AS
Can add additional levels of hierarchy
And can do flat routing at each level
  Address can be both locator and identifier

## Slide 34: Implementing This Design
Could have had extra addresses as options…
Routers always forward on visible part of address
  Until you reach that address (AS/Network/..)
When arrive in a AS/Network you pop address
  Bringing the next address to the top
Elegant design, completely compatible with IP

## Slide 35: But that’s not what happened
Rather than reusing the lesson of hierarchy, L3 addressing has turned into a mess
Rest is a story of how a good design turned bad
To understand, we need to dive into details...

## Slide 36: Gory Details of Addressing

## Slide 37: IP Addresses (IPv4)
Unique 32-bit number associated with an interface
  on a host, on a router, … connect to ports, links, etc.
  Association can be long-term or short-term
Use dotted-quad notation, e.g., 12.34.158.5:
00001100
00100010
10011110
00000101
12
34
158
5

## Slide 38: Examples
What address is this?
How would you represent 68.115.183.7?
01010000
00010011
11110000
00110011
01000100
01110011
10110111
00000111
80.19.240.51

## Slide 39: Original Internet Addresses
First eight bits: network address (/8)
  Slash notation indicates network address
Last 24 bits: host address
Assumed 256 networks were more than enough!

## Slide 40: Nice Features
Transit routers looked at what portion of address?
  Network
That portion of address space was flat
  No need for hierarchy with 256 entries
Rest of address only relevant on host’s network
But did not provide for enough networks
  Ubiquity of ethernet not foreseen

## Slide 41: Next Design: Classful Addressing
  Class A: if first byte in [0..127]  assume /8 (top bit = 0)
    Very large blocks (e.g., MIT has 18.0.0.0/8)
  Class B: first byte in [128..191]  assume /16 (top bits = 10)
    Large blocks (e.g,. UCB has 128.32.0.0/16)
  Class C: [192..223]  assume /24 (top bits = 110)
    Small blocks (e.g., ICIR has 192.150.187.0/24)
    (My house used to have a /25)
0*******
********
********
********
10******
********
********
********
110*****
********
********
********
126 nets
~16M hosts
~16K nets
~65K hosts
~2M nets
254 hosts

## Slide 42: Classful Addressing (cont’d)
  Class D: [224..239] (top bits 1110)
    Multicast groups
  Class E: [240..255] (top bits 11110)
    Reserved for future use
1110****
********
********
********
11110***
********
********
********
Multicast
Experimental
Nice feature of design:
  First bits tell you which is network address

## Slide 43: What is wrong with classful?
Only comes in 3 sizes
Routers may need state for many class C’s (/24s)
Wasted address space

## Slide 44: Today’s Addressing: CIDR
CIDR = Classless Interdomain Routing
Flexible division between network and host addresses
Must specify both address and mask
  Clarifies where boundary between addresses lies
  Classful addressing communicate this with first few bits
  CIDR requires explicit mask
Mask carried in routing algorithm
  Not implicitly carried in address

## Slide 45: Hierarchical Addressing
Prefix is network address: suffix is host address
12.34.158.0/23 is a 23-bit prefix with 29 addresses
  Terminology: “Slash 23”
00001100
00100010
10011110
00000101
Network (23 bits)
Host (9 bits)
12
34
158
5

## Slide 46: IP Address and a 23-bit Subnet Mask
00001100
00100010
10011110
00000101
12
34
158
5
11111111
11111111
11111110
00000000
255
255
254
0
Address
Mask

## Slide 47: CIDR Addressing
IP Address : 12.4.0.0 IP Mask: 255.254.0.0
00001100
00000100
00000000
00000000
11111111
11111110
00000000
00000000
Address
Mask
for hosts
Network Prefix
Use two 32-bit numbers to represent a network.
Network number = IP address + Mask
Written as 12.4.0.0/15 or 12.4/15

## Slide 48: Classful vs. Classless addresses
Example: an organization needs 500 addresses.
  A single class C address not enough (254 hosts).
  Instead a class B address is allocated. (~65K hosts)
  That’s overkill, a huge waste!
CIDR allows an arbitrary prefix-suffix boundary
  Hence, organization allocated a single /23 address (equivalent of 2 class C’s)
Maximum waste: 50%

## Slide 49: How Do Prefixes Help?
Number nearby hosts with same prefix
  1.2.3.0/24 on the left LAN
  5.6.7.0/24 on the right LAN
host
host
host
LAN 1
...
host
host
host
LAN 2
...
router
router
router
WAN
WAN
1.2.3.4
1.2.3.7
1.2.3.156
5.6.7.8
5.6.7.9
5.6.7.212
1.2.3.0/24
5.6.7.0/24
forwarding table
Notes: What are the routing entries?

## Slide 50: Easy to Add New Hosts
No need to update the routers
  E.g., adding a new host 5.6.7.213 on the right
  Doesn’t require adding a new forwarding entry
host
host
host
LAN 1
...
host
host
host
LAN 2
...
router
router
router
WAN
WAN
1.2.3.4
1.2.3.7
1.2.3.156
5.6.7.8
5.6.7.9
5.6.7.212
1.2.3.0/24
5.6.7.0/24
forwarding table
host
5.6.7.213

## Slide 51: “Subnet” Terminology
Think of LANs as special case of “subnets”
  Subnet is region without routers containing addresses within the “subnet mask”, could be a link, or LAN
  Area with same network address
Textbook has an operational definition of subnet
  Remove all interfaces from hosts, routers
  The regions that remain connected are subnets
Subnets are the lowest level of aggregation
  No routers needed within a subnet
  But you might have switches (L2)

## Slide 52: Aggregation
All of this is about aggregation

## Slide 53: Aggregation only works if….
Groups of addresses require same forwarding
These groups are contiguous in address space
These groups are relatively stable
Few enough groups to make forwarding easy

## Slide 54: CIDR: Hierarchal Address Allocation
Prefixes are key to Internet scalability
  Addresses allocated in contiguous chunks (prefixes)
  Routing protocols and packet forwarding based on prefixes
  Recursively break down chunks as get closer to host
12.0.0.0/8
12.0.0.0/15
12.253.0.0/16
12.2.0.0/16
12.3.0.0/16
:
:
12.3.0.0/22
12.3.4.0/24
:
:
12.3.254.0/23
12.253.0.0/19
12.253.32.0/19
12.253.64.0/19
12.253.64.108/30
12.253.96.0/18
12.253.128.0/17
:
:
:
:

## Slide 55: Allocation Done Hierarchically
Internet Corporation for Assigned Names and Numbers (ICANN) gives large blocks to…
  Regional Internet Registries, such as the American Registry for Internet Names (ARIN), which give blocks to…
Large institutions (ISPs), which give addresses to…
Individuals and smaller institutions
FAKE Example:
ICANN  ARIN  AT&T  UCB  EECS

## Slide 56: FAKE Example in More Detail
ICANN gives ARIN several /8s
ARIN gives AT&T one /8, 12.0/8
  Network Prefix: 00001100
AT&T gives UCB a /16, 12.197/16
  Network Prefix: 0000110011000101
UCB gives EECS a /24, 12.197.45/24
  Network Prefix: 000011001100010100101101
EECS gives me a specific address 12.197.45.23
  Address: 00001100110001010010110100010111

## Slide 57: Why Is Aggregation Nontrivial?
Mobility: laptops, cellphones, etc.
  Not really….Dynamic address assignment
Multihoming: Many entities have two or more ISPs
Institutional renumbering hard

## Slide 58: IP addressing  scalable routing?
Hierarchical address allocation only helps routing scalability if allocation matches topological hierarchy

## Slide 59: Scalability: Address Aggregation
Provider is given 201.10.0.0/21 (201.10.0.x .. 201.10.7.x)
201.10.0.0/22
201.10.4.0/24
201.10.5.0/24
201.10.6.0/23
Provider
Routers in the rest of the Internet just need to know how to reach 201.10.0.0/21. The provider can direct the IP packets to the appropriate customer.

## Slide 60: Aggregation Not Always Possible
201.10.0.0/21
201.10.0.0/22
201.10.4.0/24
201.10.5.0/24
201.10.6.0/23
Provider 1
Provider 2
Multi-homed customer with 201.10.6.0/23 has two providers. Other parts of the Internet need to know how to reach these destinations through both providers.
 /23 route must be globally visible

## Slide 61: IP addressing  scalable routing?
AT&T a.0.0.0/8
France Telecom
LBL a.b.0.0/16
UCB a.c.0.0/16
a.c.*.* is this way
a.b.*.* is this way

## Slide 62: IP addressing  scalable routing?
AT&T a.0.0.0/8
France Telecom
LBL a.b.0.0/16
UCB a.c.0.0/16
a.*.*.* is this way
Can add new hosts/networks without updating
the routing entries at France Telecom
foo.com a.d.0.0/16

## Slide 63: IP addressing  scalable routing?
AT&T a.0.0.0/8
LBL a.b.0.0/16
UCB a.c.0.0/16
ESNet
ESNet must maintain routing entries for both a.*.*.* and a.c.*.*

## Slide 64: IP addressing  scalable routing?
Hierarchical address allocation helps routing scalability if allocation matches topological hierarchy
Problem: may not be able to aggregate addresses for “multi-homed” networks
Two competing forces in scalable routing
  aggregation reduces number of routing entries
  multi-homing increases number of entries

## Slide 65: Growth in Routed Prefixes (1989-2005)
Initial growth super-linear; no aggregation
Advent of CIDR allows aggregation: linear growth
Internet boom: multihoming drives superlinear growth
Dot-com implosion; Internet bubble bursts
Back in business

## Slide 66: Same Table, Extended to Present
Stock Market
Crash of 2008
What Happened Here?
Linear growth
Superlinear growth

## Slide 67: Summary of Addressing
Hierarchical addressing
  Critical for scalable system
  Don’t require everyone to know everyone else
  Reduces amount of updating when something changes
Non-uniform hierarchy
  Useful for heterogeneous networks of different sizes
  Class-based addressing was far too coarse
  Classless InterDomain Routing (CIDR) more flexible
But how do you forward on these addresses?

## Slide 68: Challenge
How do you keep table small even with holes in aggregation?
For next time….