## Slide 1: Packets in Flight
CS 168 – Fall 2016 – Section 2

## Slide 2: Packets in Flight
When we send packets…
  ... some of them get to the destination
  ... some don’t
  ... some get there fast
  ... some take longer
  Why does this happen?

## Slide 3: Packets in Flight- Delays
How long does it take for your data to reach its destination?
It depends on…
  ... how much data you’re sending and the link speed  transmission delay
  ... your distance from the destination  propagation delay
  … the traffic pattern  queuing delay
  … how fast routers process the packet header  processing delay
Notes: Transmission – how long it takes computer to actually put bits onto the wire. Depends on how much data you’re sending and the link speed
Propagation – normally speed of light.
Queueing – the traffic pattern. Routers are usually receiving/sending many packets on many different connections simultaneously, and this can slow down the network.

## Slide 4: Packets in Flight- Delays
How long does it take for your data to reach its destination?
It depends on…
  ... how much data you’re sending and the link speed  transmission delay
  ... your distance from the destination  propagation delay
  … the traffic pattern  queuing delay
  … how fast routers process the packet header  processing delay
We will ignore processing delay
Notes: Processing – not really gonna talk about them

## Slide 5: Transmission Delay
How long it takes for the all bits in the packet to get on the wire
    The time between the first and last bits enter the link
Notes: test

## Slide 6: Transmission Delay
Longer time between first and last bits getting on the wire
How long it takes for the all bits in the packet to get on the wire
    The time between the first and last bits enter the link
  Limited by the bandwidth
Notes: Bandwidth – how many bits you can send through a wire per second

## Slide 7: Transmission Delay
How long it takes for the all bits in the packet to get on the wire
    The time between the first and last bits enter the link
  Limited by the bandwidth
  Depends on packet size
Notes: Transmission delay depends on packet size: the more data you have to send, the longer it’s gonna take to put that data onto the wire. You can only put so many bits onto the wire per second

## Slide 8: Transmission Delay
How long it takes for the all bits in the packet to get on the wire
    The time between the first and last bits enter the link
  Limited by the bandwidth
  Depends on packet size
Transmission delay
=
packet size (bytes)
/ bandwidth (bits/sec)
Notes: Packet size = bytes
Bandwidth = bytes per second

## Slide 9: Transmission Delay: Example
Bandwidth = 4 Mbps
Packet size = 500B
1 Mbps = 10^6 bits per second
1 ms = 10^3 seconds
Transmission delay =
(packet size) / bandwidth

## Slide 10: Transmission Delay: Example
Bandwidth = 4 Mbps
Packet size = 500B
1 Mbps = 10^6 bits per second
1 ms = 10^3 seconds
Transmission delay =
(packet size) / bandwidth

## Slide 11: Propagation Delay (latency)
How long it takes to transmit one bit from one end to the other
Depends on the length of the link
Limited by the speed of light (propagation speed of link)
Does NOT depend on the size of the packet
Propagation Delay
=
length of link (m)
/ speed of light (m / sec)

## Slide 12: Propagation Delay: Example
Propagation Delay
=
(link length) / (link speed)
Link speed = speed of light
≈ 3 * 10^5 km/s
Link length = 6000 km

## Slide 13: Propagation Delay: Example
Propagation Delay
=
(link length) / (link speed)
Link speed = speed of light
≈ 3 * 10^5 km/s
Link length = 6000 km

## Slide 14: Bandwidth Delay Product (BDP)
Now that we know the propagation delay, we can tell how many bits are “in flight” (on the link) at any time
??
??
BDP = ?? * ??

## Slide 15: Bandwidth Delay Product (BDP)
Now that we know the propagation delay, we can tell how many bits are “in flight” (on the link) at any time
Bandwidth
Propagation delay
BDP = Bandwidth * Propagation delay

## Slide 16
Packets might have to wait before they can be transmitted…

## Slide 17: Queuing Delay
How long the packet waits to get on the wire
Happens when arrival rate is greater than transmission rate
Depends on arrival rate, transmission rate, burstiness

## Slide 18: Queues
http://www.ccs-labs.org/teaching/rn/animations/queue/index.htm
  (emission rate is our “arrival rate”)
  What happens when emission rate > transmission rate?
How does burstiness affect queuing delays?
What happens when the queue is full?

## Slide 19: Queues
http://www.ccs-labs.org/teaching/rn/animations/queue/index.htm
  (emission rate is our “arrival rate”)
  What happens when emission rate > transmission rate?
How does burstiness affect queuing delays?
  Bursty flows tend to increase queuing delay
What happens when the queue is full?
  Packets are dropped

## Slide 20: End-to-end Delay
Sum of all nodal delays on the path

## Slide 21: Round Trip Time (RTT)
The time it for the packet to reach its destination…
… and receive a response

## Slide 22: Visualizing packet delay…
Transmission delay
Propagation delay
Time

## Slide 23: Visualizing end-to-end delay…
Transmission delay
Propagation delay
Transmission delay
Propagation delay
Time
A
R
B

## Slide 24: Visualizing end-to-end delay…
Transmission delay
Propagation delay
Transmission delay
Propagation delay
What is this??
Time
Two packets, back-to-back
End-to-end delay of brown packet

## Slide 25: Visualizing end-to-end delay…
Transmission delay
Propagation delay
Transmission delay
Propagation delay
Queuing delay
Time
Two packets, back-to-back
End-to-end delay of brown packet