## Slide 1: CS 168 How the Internet Works
Fall 2016
Scott Shenker
CS168.io
http://inst.eecs.berkeley.edu/~cs168/fa16/

## Slide 2
Ssssshhhhhhhhhhhhhhh

## Slide 3: Administrivia
Discussion sections start tomorrow
  Bring your laptop!
First project out: Alice Sheng lead TA
  Project OH: every weekday 4-6 (Soda 415/420)
  Due in a week+. First part in section tomorrow.
Next lecture: philosophy, principles,…
Next week: routing!

## Slide 4: Today’s Lecture
Overview of how the Internet works
Why packets?
Packet dynamics
  Delays, queues, and all that….
  This stuff is boring, ask questions earlier

## Slide 5: Networks Deliver Packets
end-system
switch
link
packet
path

## Slide 6: The Core Task of Internet
Delivers packets between processes (applications) on different hosts
  This involves both the network and network stack
Network: Routers/switches and links
Network stack: networking SW on host
  Stack replicates some router/switch functionality
  Then adds some additional networking functionality…
  ...before handing body of packet to application
  Will discuss this in next lecture

## Slide 7: Packets
Packets are bags of bits with:
  Header: meaningful to network (and network stack)
    Can be more than one header!
  Body: meaningful only to application
Body can be bits in a file, image, whatever
What information goes in a header?
Header
Body
Used By Network
Used By App

## Slide 8: Packets Must Be Sent Along Path
end-system
switch
link
packet
path

## Slide 9: What Must Header Contain For This?
Packet must describe where it should be sent
Requires an address for the destination host
That’s the only way a router/switch can know what to do with the packet

## Slide 10: Names vs Addresses
Network address: where host is located
Network name: which host it is
When you move server to new building
  Name doesn’t change
  But address does
Same thing with your own name and address!
Let’s get back to packet delivery….

## Slide 11: Packets Must Be Sent Along Path
end-system
switch
link
packet
path

## Slide 12: Fundamental Challenge #1
Route packets through network to destination
Given destination address, how does each switch/router forward packets so that packet reaches destination?
When a packet arrives at a router, the routing table determines which outgoing link the packet is sent on
  Outgoing link is often referred to as a port
  The word port has two meanings in this lecture

## Slide 13: Two Meanings of “Port”
Switches/routers have physical ports:
  Places where links connect to switches
Network stacks have logical ports:
  Logical places where applications connect to stack
  More about this later in lecture, and in section
Back to routing tables…
  Where do they come from?

## Slide 14: Routing Protocols (Conceptually)
Distributed algorithm run between routers
Gather information about the network topology
Compute paths through that topology
Store forwarding information in each router:
  If packet is destined for X, send out this port
  If packet is destined for Y, send out that port
  …
We call this a routing table

## Slide 15: Control Plane vs Data Plane
Control plane: mechanisms used to compute routing tables (and other forwarding information)
  Inherently global: must know topology to compute
  Routing algorithm is part of the control plane
  Time scale: per network event
Data plane: using those tables to actually forward packets
  Inherently local: depends only on arriving packet and local routing table
  Forwarding mechanism is part of data plane
  Time scale: per packet arrival

## Slide 16: Fundamental Challenge #2
How do you deliver packets reliably?
Packets can be dropped along the way
  Buffers in router can overflow
  Routers can crash while buffering packets
  Links can garble packets
How do you make sure packets arrive safely on an unreliable network?
  Or at least know if they are not delivered….
  Want no false positives, and high chance of success

## Slide 17: Two Questions about Reliability
Who is responsible for this? (architecture)
  Network?
  Host?
How is it implemented? (engineering)
We will consider both perspectives….

## Slide 18: Other Important Challenges
Routing with autonomous control
  Internet is comprised of many different ISPs
  More generally called Autonomous Systems (ASes)
  They each get to make their own decisions about how to do routing
  How can you make sure that these independent decisions result in usable end-to-end routes?
Congestion control
  Hosts on the Internet independently decide at what rate they will send packets
  How can you make sure that these independent decisions don’t overload various links?

## Slide 19: What Have We Missed?
Consider when you access a web page
  Insert URL into browser (e.g., cnn.com)
  Packets sent to web site (reliably)
  Packets reach application on destination host
How do you get to the web site?
  URL is user-level name (e.g., cnn.com)
  Network needs address (e.g., where is cnn.com?)
Must map names to addresses….

## Slide 20: Mapping Names to Addresses
On the Internet, we only name hosts (sort of)
  URLs are based on the name of the host containing the content (i.e., cnn.com names a host)
Before you can send packets to cnn.com, you must resolve names into the host’s address
Done by the Domain Name System (DNS)

## Slide 21: Finishing Our Story
We now have the address of the web site
  So we can send packets to host
  Are we done?
When a packet arrives at a host, what does the host do with it?
  To which process (app) should the packet be sent?
If the packet header only has the destination address, how does the host know where to deliver packet?

## Slide 22: Of Sockets and Ports
When a process wants access to the network, it opens a socket, which is associated with a port
  This is not a physical port, just a logical one
Socket: an OS mechanism that connects processes to the networking stack
Port: number that identifies that particular socket
The port number is used by the OS to direct incoming packets

## Slide 23: Implications for Packet Header
Packer header includes:
  Destination address and port
  Source address and port
When a packet arrives, packet is delivered to socket associated with the destination port
Why include the source port/address?
Details about sockets in section (tomorrow!)

## Slide 24: Separation of Concerns
Network
  Deliver packets from host to host (based on address)
Network Stack (OS)
  Deliver packets to appropriate socket (based on port)
Applications
  Send and receive packets
  Understand content of packet bodies
Secret of the Internet’s success is getting these and other abstractions right…

## Slide 25: Review of Important Issues
Routing
Reliable transport
Routing with autonomous control
Congestion control
Mapping names to addresses

## Slide 26: What Else Are We Missing?
How do hosts get their addresses?
  DHCP
What else happens to packets on path?
  Middleboxes
What about security?
  Names play a central role. Why?
What about specialized networks?
  Wireless, Datacenters, Ethernets (L2)
Notes: This completes the list of topics we will cover…

## Slide 27: Why Packets?

## Slide 28: Links/Switches are Shared
shared link and switch resources

## Slide 29: Two approaches to sharing
Reservations:
  “Flows” reserve bandwidth needed in advance
  Must reserve their peak bandwidth
On demand: (also known as “best effort”)
  Send packets when you have them
  Hope for the best….

## Slide 30: Example of Statistical Multiplexing
Statistical multiplexing: Combining demands to share resources efficiently
  Long history in computer science
    Processes on an OS
    Cloud computing
Based on the premise that:
  Peak of aggregate load is << aggregate of peak loads
  In fact peak of agg. approaches sum of average loads
Therefore, it is better to share resources than to strictly partition them….

## Slide 31: Two Design Choices
Both embody statistical multiplexing
Reservation: sharing at flow level
  Resources shared between flows currently in system
On-demand: sharing at packet level
  Resources shared between packets currently in system

## Slide 32: Two approaches to sharing
Reservations
On demand
How are these implemented?

## Slide 33: Two approaches to sharing
Reservations  circuit switching
  Set up a “circuit”, no need to look at individual packet headers in detail
On demand  packet switching
  Service each packet independently by inspecting its packet header
How are these implemented?

## Slide 34: Circuit Switching
(1) src sends a reservation request for 10Mbps to dst
(2) Switches “establish a circuit”
(3) src starts sending data
(4) src sends a “teardown circuit” message
dst
10Mb/s?
10Mb/s?
10Mb/s?
src
✔
✔
✔

## Slide 35: Circuit Switching
switch
src
dst
Reservation also establishes a “circuit” within a switch

## Slide 36: Many kinds of “circuits”
Time division multiplexing
  divide time in time slots
  separate time slot per circuit
Frequency division multiplexing
  divide frequency spectrum in frequency bands
  separate frequency band per circuit
time
time
frequency

## Slide 37: Circuit Switching and Failures
A
B
Circuit switching doesn’t “route around trouble”
Circuit is established
Link Fails along path
Must establish new circuit

## Slide 38: Packet switching
switch
dst
Each packet contains destination (dst)
Each packet treated independently

## Slide 39: Packet switching
With buffers to absorb transient overloads
switch
dst
Each packet contains destination (dst)
Each packet treated independently

## Slide 40: Packet Switching and Failures
A
B
Packet switching “routes around trouble”
Link Fails along path
Route recomputed on the fly

## Slide 41: Which is better: Circuits or Packets?
What are the tradeoffs?
Which is better for the Internet?

## Slide 42: Example: three constant sources
Total bandwidth 30Mbps
  Mbps = megabits per second
Demands: Each source needs a constant rate of 10Mbps
Reservation and on-demand give same result
  Every source gets what they need
  No wasted bandwidth
  ….

## Slide 43: Example: Three “bursty” sources
12Mbps
Time
Link capacity = 30Mbps
11Mbps
13Mbps

## Slide 44: What happens with reservations?
12Mbps
Option #1: allow two flows to reserve peak rate
Time
Link capacity = 30Mbps
11Mbps
13Mbps
Must turn away third flow!

## Slide 45: What happens with reservations?
12Mbps
Option #2: allow flows to reserve equal rates
Time
11Mbps
13Mbps
Link capacity = 30Mbps
Each source gets 10Mbps
Frequent overloading!

## Slide 46: What happens with on-demand?
No overloading
Time
Link capacity = 30Mbps

## Slide 47: Peak vs Average Rates
For each flow, define:
  P = peak rate
  A = average rate
Reservations must reserve P:
  But flows only use A (on average)
  Level of utilization is A/P
On-demand:
  Can achieve higher utilizations
  Depends on degree of sharing, burstiness of flows
  Peak of aggregate approaches sum of averages

## Slide 48: Smooth vs Bursty Applications
Some apps have relatively small P/A ratios
  Voice might have a ratio of 3:1 or so
Data applications tend to be rather bursty
  Ratios of 100 or greater are common
That’s why the phone network used reservations
  And the Internet does not….
  More in next lecture (not as obvious as it may seem)

## Slide 49: Packet Delays

## Slide 50: Performance Metrics
Delay
Loss
Throughput

## Slide 51: Delay
How long does it take to send a packet from its source to destination?

## Slide 52: Loss
What fraction of the packets sent to a destination are dropped?

## Slide 53: Throughput
At what rate is the destination receiving data from the source?

## Slide 54: Today
Focus on delay
Loss and throughput will become relevant in later lectures….

## Slide 55: A network link
Link bandwidth
  Number of bits sent per unit time (bits/sec or bps)
Propagation delay (sometimes called latency)
  Time for one bit to move through the link (seconds)
Bandwidth-Delay Product (BDP)
  Number of bits “in flight” at any time (sent, not recvd)
  BDP = bandwidth × propagation delay
bandwidth
Propagation delay
delay x bandwidth

## Slide 56: Examples of BDP
Same city over a slow link:
  bandwidth: ~100Mbps
  propagation delay: ~0.1msec
  BDP: 10,000bits (1.25KBytes)
Between cities over fast link:
  bandwidth: ~10Gbps
  propagation delay: ~10msec
  BDP: 108bits (12.5MBytes)

## Slide 57: Delay
Consists of four components
  Transmission delay
  Propagation delay
  Processing delay
  Queueing delay
First consider transmission, propagation delays
Then queueing delays
Ignore processing delays (tiny in most cases)
due to link properties
due to traffic mix and
switch internals

## Slide 58
transmission
End-to-end delay
propagation
queuing
processing
transmission
propagation
queuing
processing
transmission
propagation

## Slide 59: Transmission Delay
Q: How long does it take to push all the bits of a packet into a link?
A: Packet size / Transmission rate of the link
Example: Packet = 1kb, Rate = 100Mbps
  1000 bits / 100 Mbits per sec = 10-5 sec = 10μsec

## Slide 60: Propagation Delay
Q: How long does it take to move one bit from one end of a link to the other?
A: Link length / Propagation speed of link
  Propagation speed ~ some fraction of speed of light
Example: Length = 30 kilometers
  30 kilometers/3x108 meters per sec = 10-4 sec = 100μsec

## Slide 61: Now ask a more practical question
Q: How long does it take for a packet to travel from A to B?
A: The delay combines both transmission and propagation delays
  Perhaps also queueing, but ignore those for now

## Slide 62: Example: 100B packet from A to B
time=0
A
B
100Byte packet
Time
1Mbps, 1ms
Time to transmit one bit = 1/106s
Time to transmit 800 bits=800x1/106s
Time when that bit reaches B = 1/106+1/103s
The last bit reaches B at
(800x1/106)+1/103s
= 1.8ms
This is exactly
transmission
plus propogation
delays!

## Slide 63: Example: 100B packet from A to B
A
B
100Byte packet
Time
1Mbps, 1ms
1Gbps, 1ms?
The last bit reaches B at
(800x1/106)+1/103s
= 1.8ms
1GB file in 100B packets
The last bit reaches B at
(800x1/109)+1/103s
= 1.0008ms
The last bit in the file reaches B at
(107x800x1/109)+1/103s
= 8001ms
107 x 100B packets

## Slide 64: Three cases with 1msec prop. delay
1GB file, 1Gbps link: transmission time dominant
100B packet, 1Gbps link: propagation delay dominant
100B packet, 1Mbps link: transmission ~ propagation
Network design might differ based on which dominates
  But in the Internet, can’t know in advance!

## Slide 65: Technology Trends
Propagation delay?
  No change
Transmission delay?
  Getting smaller!
Queueing delay?
  Usually smaller
How does this affect applications?
  CDNs work very hard to move data near clients
  Reduces backbone bandwidth requirements
  But also decreases latency
  Google: time is money!

## Slide 66: What Trend Did I Leave Out?
The dominance of video
Very high fraction of traffic is video
Files getting larger
But also many, many small flows…
Crucial aspect of Internet traffic:
  Most flows are tiny
  Most bytes in large flows
  Can’t only design for either end of the spectrum

## Slide 67: Another way of visualizing packets and their delays

## Slide 68: The “pipe” view
A
B
100Byte packet
Time
1Mbps, 10ms
100Byte packet
100Byte packet
time 
BW 
pkt tx time

## Slide 69: The “pipe” view
1Mbps, 10ms (BDP=10,000)
time 
BW 
10Mbps, 1ms (BDP=10,000)
time 
BW 
1Mbps, 5ms (BDP=5,000)
time 
BW 

## Slide 70: The “pipe” view
1Mbps, 10ms (BDP=10,000)
time 
BW 
1Mbps, 10ms (BDP=10,000)
time 
BW 
100b packets
250b packets

## Slide 71: Queueing and Packet Dynamics

## Slide 72: Queueing delay: “pipe” view

## Slide 73: Queueing delay: “pipe” view
No overload!

## Slide 74: Queueing delay: “pipe” view
Transient Overload
Not a rare event!
Queue

## Slide 75: Queueing delay: “pipe” view
Queue
Transient Overload
Not a rare event!

## Slide 76: Queueing delay: “pipe” view
Queue
Transient Overload
Not a rare event!

## Slide 77: Queueing delay: “pipe” view
Queue
Transient Overload
Not a rare event!

## Slide 78: Queueing delay: “pipe” view
Queue
Transient Overload
Not a rare event!

## Slide 79: Queueing delay: “pipe” view
Queue
Transient Overload
Not a rare event!
Queues absorb transient bursts but introduce queueing delay

## Slide 80: Queueing delay: “pipe” view
What about persistent overload?
Will eventually drop packets (“loss”)

## Slide 81: More packet animations….

## Slide 82: The Lifecycle of Packets
Excess Packets
Stored in Buffer
Packet Arriving
at Switch
Packet
Being
Transmitted
Packet Buffer
Link
Packet Currently
Being Transmitted

## Slide 83: The Delays of Their Lives
Queueing
Delay
Transmission
Delay
Propagation Delay is how long it takes
to reach the next switch after transmission
Round-Trip Time (RTT) is the time it takes
a packet to reach the destination and
the response to return to the sender

## Slide 84: Smooth Arrivals = No Queueing Delays

## Slide 85: Bursty Arrivals = Queueing Delays
There is substantial queueing delay even though link is underutilized

## Slide 86: Packet Losses: Buffers Full

## Slide 87: Packet Losses: Corruption

## Slide 88: Queueing Delay
How long does a packet have to sit in a buffer before it is processed?
Depends on traffic pattern
  Arrival rate at the queue
  Nature of arriving traffic (bursty or not?)
  Transmission rate of outgoing link

## Slide 89
arrival rate / departure rate
1
Average queuing delay
Notes: This plot shows the average queuing delay experienced by a packet arriving at a buffer,
as a function of this entity here, which is the arrival rate divided by the departure rate.
As this entity approaches 1 (the arrival rate approaches the departure rate),
the average delay goes to infinity.
The important thing to note about this curve is the shape.
When we approach close to this area here, the curve goes up very fast.
This means that small changes in arrival rate can have a dramatic impact on delay.
This is what happens when you are driving in a congested highway.
The smallest disturbance (like one car braking) can significantly increase your delay.
When you design a queuing system, you want it to operate far from that point.

## Slide 90: Basic Queueing Terminology
Arrival process: how packets arrive
  Average rate A
  Peak rate P
W: average time packets wait in the queue
  W for “waiting time”
L: average number of packets waiting in the queue
  L for “length of queue”

## Slide 91: Little’s Law (1961)
L = A x W
Compute L: count packets in queue every second
  How often does a single packet get counted? W times
Why do you care?
  Easy to compute L and A, harder to compute W
Congratulations, you now know all the queueing theory you ever need to know!

## Slide 92: Thursday’s lecture….
Layering, principles, the “good stuff”
Read K&R 1.4-1.8 (mostly for context)