## Slide 1: CS 168 Designing the Internet
Fall 2016
Scott Shenker
CS168.io
http://inst.eecs.berkeley.edu/~cs168/fa16/

## Slide 2
Ssssshhhhhhhhhhhhhhh

## Slide 3: About My Previous Lecture
The Internet is a huge, complicated system
One can study the parts in isolation
  Routing
  Congestion control
  ….
But the pieces all fit together in a particular way
Tuesday’s lecture was a quick overview of how these pieces fit together...
  Don’t worry if you didn’t understand much of it
  You probably absorbed more than you realize

## Slide 4: At the end of today’s lecture you…
…will have heard Internet’s “why” and “when”
  Not the “how”….that will take the rest of the semester
You won’t understand it all, but that’s ok
  Useful context before diving into details
  And review these slides every few weeks
Do not worry about details of how things work
  This is an “architectural” lecture
Notes: Refer to last lecture

## Slide 5: Outline for Today
Modularity (technical)
Layering (technical)
Design principles (technical)
If the Internet is the answer, what were the questions? (context)
History of the Internet (context)
Design goals of the Internet (both)

## Slide 6: No deep technical issues
Invention of the Internet not due to cleverness…
…but to wisdom
The inventors asked the right questions…
  …and were willing to “think differently” to answer them
But there were no technology breakthroughs…
  …or brilliant algorithms

## Slide 7: Modularity

## Slide 8: What is Modularity?
Modularity is nothing more than decomposing programs/systems into smaller units
Plays a crucial role in computer science…
...and networking

## Slide 9: Modularity in Computer Science
“Modularity based on abstraction is the way things get done”
--Barbara Liskov

## Slide 10: The Role of Modularity
We can’t build big systems out of spaghetti code
  Impossible to understand, debug
  Hard to update
We need to limit the scope of changes, so that we can update system without rewriting it from scratch
Modularity is how we limit the scope of changes
  And understand the system at a higher level

## Slide 11: Computer System Modularity
Partition system into modules
  Each module has well-defined interface
Interfaces give flexibility in implementation
  Changes have limited scope
Examples:
  Libraries encapsulating set of functionality
  Programming language abstracts away CPU
The trick is to find the right modularity
  The interfaces should be long-lasting
  If interfaces are changing often, modularity is wrong

## Slide 12: Finding the Right Modularity
Decompose problem into tasks or abstractions
  Task: e.g., compute a function
  Abstraction: e.g., provide reliable storage
Define a module for each task/abstraction
  Involves defining a clean interface for each module
  “Clean” means hiding unnecessary details
Implement system a few times:
  If interfaces seem to hold, you are on the right track…

## Slide 13: Network System Modularity
The need for modularity still applies
  And is even more important! (why?)
Network implementations not just distributed across many lines of code
  Normal modularity “organizes” that code
Networking is distributed across many machines
  Hosts
  Routers

## Slide 14: Network Modularity Decisions
How to break system into modules?
  Classic decomposition into tasks
Where are modules implemented?
  Hosts?
  Routers?
  Both?
Where is state stored?
  Hosts?
  Routers?
  Both?

## Slide 15: Leads to three design principles
How to break system into modules?
  Layering
Where are modules implemented?
  End-to-End Principle
Where is state stored?
  Fate-Sharing

## Slide 16: Layering

## Slide 17: Tasks in Networking
What does it take to send packets across country?
Simplistic decomposition:
  Task 1: send along a single wire
  Task 2: stitch these together to go across country
This gives idea of what I mean by decomposition
Next slide presents a much more detailed version
Notes: How would you decompose networking into tasks???

## Slide 18: Breakdown into Tasks
Bits on wire
Packets on wire
Deliver packets to host across local network
  Local addresses
Deliver packets to host across country
  Global addresses
Deliver packets reliably, to correct process
Do something with the data

## Slide 19: Resulting Modules (layers)
Bits on wire (Physical)
Packets on wire (contained in next layer)
Deliver packets across local network (Datalink)
  Local addresses
Deliver packets across country (Network)
  Global addresses
Deliver packets reliably to process (Transport)
Do something with the data (Application)

## Slide 20: Five Layers (top-down)
Application: Providing network support for apps
Transport (L4): (Reliable) end-to-end delivery
Network (L3): Global best-effort delivery
Datalink (L2): Local best-effort delivery
Physical: Bits on wire
Interactions between these components?
  Do all components talk to each other?
  Or are the components limited in their interactions?
Answer: they are strictly layered!

## Slide 21: Strictly Layered Dependencies
Applications
…built on…
…built on…
…built on…
…built on…
Reliable (or unreliable) transport
Best-effort global packet delivery
Best-effort local packet delivery
Physical transfer of bits
Notes: Two things:
Strict layering
Talk to companion layer

## Slide 22: Three Observations
Each layer:
  Depends on layer below
  Supports layer above
  Independent of others
Multiple versions in layer
  Interfaces differ somewhat
  Components pick which lower-level protocol to use
But only one IP layer
  Unifying protocol

## Slide 23: Layering Crucial to Internet’s Success
Innovation at most levels
  Applications (lots)
  Transport (few)
  Datalink (few)
  Physical (lots)
Innovation proceeded largely in parallel
  Payoff of modularity!
Pursued by very different communities
  Like systems and chip designs

## Slide 24: Questions?

## Slide 25: Distributing Layers Across Network
Layers are simple if only on a single machine
  Just stack of modules interacting with those above/below
But we need to implement layers across machines
  Hosts
  Routers (switches)
What gets implemented where?

## Slide 26: What Gets Implemented on Host?
Bits arrive on wire, must make it up to application
Therefore, all layers must exist at host!

## Slide 27: What Gets Implemented on Router?
Bits arrive on wire
  Physical layer necessary
Packets must be delivered to next-hop
  Datalink layer necessary
Routers participate in global delivery
  Network layer necessary
Routers don’t support reliable delivery
  Transport layer (and above) not supported

## Slide 28: What Gets Implemented on Switches?
Switches do what routers do, except they don’t participate in global delivery, just local delivery
They only need to support Physical and Datalink
  Don’t need to support Network layer
Won’t focus on the router/switch distinction
  When I say switch, I almost always mean router
  Almost all boxes support network layer these days

## Slide 29: Complicated Diagram
HTTP
TCP
IP
Ethernet
interface
HTTP
TCP
IP
Ethernet
interface
IP
IP
Ethernet
interface
Ethernet
interface
SONET
interface
SONET
interface
host
host
router
router
HTTP message
TCP segment
IP packet
IP packet
IP packet

## Slide 30: Simple Diagram
Lower three layers implemented everywhere
Top two layers implemented only at hosts
Transport
Network
Datalink
Physical
Transport
Network
Datalink
Physical
Network
Datalink
Physical
Application
Application
Host A
Host B
Router
Notes: Why go up? Why not stay down in the lower levels?

## Slide 31: Physical Communication
Communication goes down to physical network
Then from network peer to peer
Then up to relevant layer
Why does packet go up to network layer in router?
Transport
Network
Datalink
Physical
Transport
Network
Datalink
Physical
Network
Datalink
Physical
Application
Application
Host A
Host B
Router
Notes: Why does it go up to network in Router?????

## Slide 32: Logical Communication
Layers interacts with peer’s corresponding layer
Transport
Network
Datalink
Physical
Transport
Network
Datalink
Physical
Network
Datalink
Physical
Application
Application
Host A
Host B
Router

## Slide 33: What Does That Mean?
Transport
Network
Datalink
Physical
Transport
Network
Datalink
Physical
Network
Datalink
Physical
Application
Application
Host A
Host B
Router
Semantic Content
Process Identity
GlobalLoc
LocalLoc

## Slide 34: Layer Encapsulation
Trans: Connection ID
Net: G Source/Dest
Link: L Src/Dest
Appl: Get index.html
User A
User B
Necessary Header Information
On wire, packet has: Local S/D, Global S/D, Transport ID, and Body
Notes: Deepest level most header

## Slide 35: Example of Layering in the Real World
CEO A writes letter to CEO B
  Folds letter and hands it to administrative aide
Aide:
  Puts letter in envelope with CEO B’s full name
  Takes to FedEx
FedEx Office
  Puts letter in larger envelope
  Puts name and street address on FedEx envelope
  Puts package on FedEx delivery truck
FedEx delivers to other company
Dear Donald,
You may have more hair, but I have more money.
--Michael

## Slide 36: The Path of the Letter
Fedex Envelope (FE)
CEO
Aide
FedEx
CEO
Aide
FedEx
Location
Letter
Envelope
Semantic Content
Identity
“Peers” on each side understand the same things
No one else needs to
Lowest level has most packaging

## Slide 37: Back to Networking Picture
Transport
Network
Datalink
Physical
Transport
Network
Datalink
Physical
Network
Datalink
Physical
Application
Application
Host A
Host B
Router
Semantic Content
Process Identity
GlobalLoc
LocalLoc

## Slide 38: Design Principles

## Slide 39: Three Internet Design Principles
How to break system into modules?
  Layering
Where are modules implemented?
  End-to-End Principle
Where is state stored?
  Fate-Sharing

## Slide 40: The End-to-End Principle
Everyone believes it, but no one knows what it means…..

## Slide 41: Placing Network Functionality
Influential paper: “End-to-End Arguments in System Design” by Saltzer, Reed, and Clark (‘84)
  End-to-end principle
Basic observation: some types of network functionality can only be correctly implemented end-to-end
In these cases, end hosts:
  Can satisfy the requirement without network’s help
  Must do so, since can’t rely on network’s help
Thus, don’t need to implement them in network
  Debate about what the network does and doesn’t do…
Notes: Contrary to wisdom of the day!
Talmud

## Slide 42: Example: Reliable File Transfer
Solution 1: make each step reliable, and string them together to make reliable end-to-end process (requires network to handle reliability)
Solution 2: allow steps to be unreliable, but do end-to-end check and try again if necessary
  False negatives but no false positives….
OS
Appl.
OS
Appl.
Host A
Host B
OK

## Slide 43: Discussion
Solution 1 cannot be made perfectly reliable
  What happens if a network element misbehaves?
  Receiver has to do the check anyway!
Solution 2 can also fail, but only if the end system itself fails (i.e., doesn’t follow its own protocol)
Solution 2 only relies on what it can control
  The endpoint behavior
Solution 1 requires endpoints trust other elements
  That’s not what reliable means!

## Slide 44: Two Notions of Reliability (Clark)
As long as the network is not partitioned, two endpoints should be able to communicate
Failures should not interfere with endpoint semantics
The second requirement implies that we must adopt solution 2 (cannot depend on network).

## Slide 45: Question?
Should you ever implement reliability in network?
Perhaps, if needed for reasonable efficiency
  Don’t aim for perfect reliability, but ok to reduce error rate
If individual links fail 10% of the time, and are traversing 10 links, then E2E error rate is 65%
Implementing two retransmissions on links
  Link error rate reduced to 0.1%, E2E error rate is 1%

## Slide 46: Back to the End-to-End Principle
Implementing such functionality in the network:
Doesn’t reduce host implementation complexity
Does increase network complexity
Often imposes delay/overhead on all applications, even if they don’t need functionality
However, implementing in network can enhance performance in some cases
  E.g., very lossy link
Three interpretations of the end-to-end principle
  Use multicast as a test case

## Slide 47: “Only-if-Sufficient” Interpretation
Don’t implement a function at the lower levels of the system unless it can be completely implemented at this level
  This argues that multicast can be built in network
Unless you can relieve the burden from hosts, don’t bother

## Slide 48: “Only-if-Necessary” Interpretation
Don’t implement anything in the network that can be implemented correctly by the hosts
  This argues that multicast should not be built in network
Make network layer absolutely minimal
  This E2E interpretation trumps performance issues
  Increases flexibility, since lower layers stay simple
Notes: One make hosts as simple as possible. The other makes the network as simple as possible. Which do you prefer?

## Slide 49: “Only-if-Useful” Interpretation
If hosts can implement functionality correctly, implement it in a lower layer only as a performance enhancement
But do so only if it does not impose burden on applications that do not require that functionality
This argues for multicast in network...

## Slide 50: Summary
Where to implement functionality is complicated
  No right or wrong answer
But everyone agrees that reliability does not belong on the network!
Multicast is a good test case

## Slide 51: Questions?

## Slide 52: What Does E2E Principle Ignore?
There are other stakeholders besides users
  ISPs care about the operation/security of their network
Some functions more easily done in the network.
  Think of firewalls…..
Thus, we need “middlebox” functionality
  Will cover later in course…

## Slide 53: Three Internet Design Principles
How to break system into modules?
  Layering
Where are modules implemented?
  End-to-End Principle
Where is state stored?
  Fate-Sharing

## Slide 54: Fate-Sharing
Note that E2E principles relied on “fate-sharing”
  Invariants break only when endpoints themselves break
  Minimize dependence on other network elements
This should dictate placement of storage

## Slide 55: General Principle: Fate-Sharing
When storing state in a distributed system, co-locate it with entities that rely on that state
Only way failure can cause loss of the critical state is if the entity that cares about it also fails ...
  … in which case it doesn’t matter
Often argues for keeping network state at end hosts rather than inside routers
  E.g., packet-switching rather than circuit-switching

## Slide 56: A Cynical View of Distributed Systems
“A distributed system is one in which the failure of a computer you didn't even know existed can render your own computer unusable”
  ---Leslie Lamport
Fate Sharing tries to prevent this!

## Slide 57: Decisions and Their Principles
How to break system into modules
  Dictated by Layering
Where modules are implemented
  Dictated by End-to-End Principle
Where state is stored
  Dictated by Fate-Sharing

## Slide 58: If the Internet is the answer, what were the questions?

## Slide 59: Internet Prehistory (late 50’s)
Telephone network is largest comm’n system
  Uses circuit switching
Need to build networks for other tasks
  Defense
  Computers
  …
But people knew that circuit switching was:
  Inefficient (for bursty loads)
  Not resilient
    Which is why AT&T worked so hard to make components reliable

## Slide 60: Three crucial questions arose
Paul Baran (RAND) asked:
  “How can we design a more resilient network?”
  And invented the notion of packet switching
Len Kleinrock (UCLA) asked:
  “How can we design a more efficient network?”
  And invented the notion of packet switching
A few years later Bob Kahn (DARPA) asked:
  “How can we connect these networks together?”
  And invented the notion of the Internet

## Slide 61: Internet Timeline
1961 Baran, Kleinrock advocate packet switching
1962 Licklider’s vision of Galactic Network
1965 Roberts connects two computers via phone
1967 Roberts publishes vision of ARPANET
1969 BBN installs first IMP at UCLA
  IMP: Interface Message Processor
1971 Network Control Program (protocol)
1972 Public demonstration of ARPANET

## Slide 62: The opening of the Internet revolution
Kleinrock’s group at UCLA tried to log on to Stanford computer: His recollection of the event…
We typed the L…
  “Do you see the L?”
  “Yes, we see the L.”
We typed the O…
  “Do you see the O?”
  “Yes, we see the O.”
Then we typed the G…
  …and the system crashed!
Notes: Perfect demo

## Slide 63: Timeline continued…
1972 Email invented
1972 Telnet introduced
1972 Kahn advocates Open Architecture networking

## Slide 64: The Problem
Many different packet-switching networks
Only nodes on the same network could communicate

## Slide 65: Kahn’s Rules for Interconnection
Each network is independent and must not be required to change (why?)
Best-effort communication (why?)
Boxes (routers) connect networks
No global control at operations level (why?)

## Slide 66: Solution
Gateways

## Slide 67: Kahn’s vision
Kahn imagined there would be only a few networks (~20) and thus only a few routers
  He was wrong (why?)
Proposed gateways to “translate” btwn networks
  Via a universal protocol that they all understood
Search for “universal” protocol is birth of Internet
  The actual design of IP came later (Cerf and Kahn)

## Slide 68: Timeline continued….
1973 FTP introduced
1973 Ethernet invented (Xerox PARC)
1974 Cerf and Kahn paper on TCP/IP
1980 TCP/IP adopted as defense standard
1983 Global NCP to TCP/IP flag day
198x XNS, DECbit, and other protocols
1984 Janet (British research network)
1985 NSFnet (picks TCP/IP) [thank you Al Gore!]
198x Internet meltdowns due to congestion
1986 Van Jacobson saves the Internet (BSD TCP)
1988 Dave Clark steps down from IAB

## Slide 69: Unsung hero of Internet: David Clark
Chief Architect 1981-1988
Great consistency of vision
Kept the Internet true to its basic design principles
Authored End-to-End Principle
Conceives and articulates architectural concepts
  Read “Active Networking and End-To-End Arguments”
Perhaps the only “irreplaceable” Internet pioneer

## Slide 70: Timeline continued…
1988 Deering and Cheriton propose multicast
1989 Birth of the web….Tim Berners-Lee (CERN)
He invented HTTP

## Slide 71: Why did it take a physicist to invent web?
Physicists are the smartest people in the world?
Computer scientists were trying to invent nirvana
  Well, actually Xanadu (Ted Nelson)
  More generally, CS researchers focused on hyptertext
Users didn’t need what we wanted to invent
  Think about it: a paper on HTTP would have been rejected by every CS conference and journal
In general, the CS research community is great at solving well-defined problems, but terrible at guessing what users will actually use
  “Academics get paid for being clever, not for being right.”
  …Don Norman

## Slide 72: Timeline continued…..
1993 Search engines invented (Excite)
1994 Internet goes commercial
199x ATM rises and falls (as internetworking layer)
Telcos try to kill the Internet
199x QoS rises and falls
I try to kill the Internet
1998 IPv6 specification
1998 Google reinvents search
200x The Internet boom and bust
201x CS enrollments suggest boom is back!
CS 168: ~80 in 2010 to >600 in 2015

## Slide 73: Internet Design Goals

## Slide 74: David Clark
Wrote a paper in 1988 that tried to capture why the Internet turned out as it did
In particular, it described an ordered list of priorities that informed the design

## Slide 75: Internet Design Goals (Clark ‘88)
Connect existing networks
Robust in face of failures
Support multiple types of delivery services
Accommodate a variety of networks
Allow distributed management
Easy host attachment
Cost effective
Allow resource accountability

## Slide 76: #1 Connect Existing Networks
Wanted single protocol that could be used to connect any pair of (existing) networks
The Internet Protocol (IP) is that unifying protocol
  All (existing) networks must be able to implement it
This is where the need for best effort arose….
  And this is where circuit switching died
  Why?

## Slide 77: #2 Robust
Def’n A: As long as network is not partitioned, two hosts should be able to communicate (eventually)
  Can recover from failures
Def’n B: Failures (excepting network partition) should not interfere with endpoint semantics
  Can isolate endpoints from failures
A: Very successful, not clear how relevant now
  Availability more important than recovering from disaster
B: This notion of robustness is underappreciated
  Key to modularity of Internet

## Slide 78: The Internet Architecture
Layer | Scope | Granularity | Where | Unique?
Application | Host | Data | Host | No
Reliability | Global | Data | Host | No
Network | Global | Packets | Network | Yes
Link | Local | Packets | Network | No
Physical | Local | Bits | Network | No

## Slide 79: The Telephony Architecture
Layer | Scope | Granularity | Where | Unique?
Application | Host | Data | Network And Host | No
Reliability | Global | Data | Network | No
Network | Global | Packets | Network | Yes
Link | Local | Packets | Network | No
Physical | Local | Bits | Network | No

## Slide 80: #3 Types of Delivery Services
Use of the term “delivery services” already implied an application-neutral network
Built lowest common denominator service
  Allow end-based protocols to provide better service
  For instance, turn unreliable service into reliable service
Example: recognition that TCP wasn’t needed (or wanted) by some applications
  Separated TCP from IP, and introduced UDP

## Slide 81: The paradox of the Internet’s design
The goal is to support many applications
These applications have different requirements
Shouldn’t the Internet support them all?
  That is, provide a service the satisfies all of them
  By meeting the most stringent requirements

## Slide 82: What service should Internet support?
Strict delay bounds?
  Some applications require them
Guaranteed delivery?
  Some applications are sensitive to packet drops
No applications mind getting good service
  Why not require Internet support all these guarantees?

## Slide 83: Important life lessons
(1) People (or applications)
Don’t always need what they think they need
Almost never need what we think they need
(2) Flexibility often more important than performance
But typically only in hindsight!
Example: cell phones vs landlines
(3) Architect for flexibility, engineer for performance
Flexibility ensures longevity
Performance requirements are ephemeral

## Slide 84: Applying lessons to Internet
Requiring performance guarantees would limit variety of networks that could attach to Internet
Many applications don’t need these guarantees
And those that do?
  Well, they don’t either (usually)
  Tremendous ability to mask drops, delays
And ISPs can work hard to deliver good service without changing the architecture (engineering)
If the Internet had focused on voice applications early, it might have made different choices

## Slide 85: Bottom Line
The choice of packet switching service is not as obvious as it might seem today
Great vision on the part of the Internet designers
And lucky that they were focused on applications that did not need great service

## Slide 86: #4 Variety of Networks
Incredibly successful!
  Minimal requirements on networks
  No need for reliability, in-order, fixed size packets, etc.
  A result of aiming for lowest common denominator
IP over everything
  Then: ARPANET, X.25, DARPA satellite network..
  Now: ATM, SONET, WDM…

## Slide 87: #5 Decentralized Management
Both a curse and a blessing
  Important for easy deployment
  Makes management hard today

## Slide 88: #6 Host Attachment
Clark observes that cost of host attachment may be higher because hosts have to be smart
But the administrative cost of adding hosts is very low, which is probably more important
  Plug-and-play kind of behavior….

## Slide 89: #7 Cost Effective
Cheaper than circuit switching at low end
More expensive than circuit switching at high end
Not a bad compromise:
  Cheap where it counts (low-end)
  More expensive for those who can pay….

## Slide 90: #8 Resource Accountability
Failure!

## Slide 91: Internet Motto
We reject kings, presidents, and voting. We believe in rough consensus and running code.”
David Clark

## Slide 92: Real Goals
Build something that works!
Connect existing networks
Robust in face of failures
Support multiple types of delivery services
Accommodate a variety of networks
Allow distributed management
Easy host attachment
Cost effective
Allow resource accountability

## Slide 93: Questions to think about….
What priorities would a commercial design have?
What would the resulting design look like?
What goals are missing from this list?
Notes: Missing: resource sharing, other considerations of malicious users (traceback, etc.), address concerns of administrative domains visible