## Slide 1: CS 168 Reliable Transport
Fall 2016
Scott Shenker
CS168.io
http://inst.eecs.berkeley.edu/~cs168/fa16/

## Slide 2
Ssssshhhhhhhhhhhhhhh

## Slide 3: Homework #1
Think of it as a worksheet, not an assignment
It is long and detailed, but contains stuff you need to know
We will release the problems later today, will release the information on how to submit answers in a few days.
Just work the problems in the meantime, and enter your answers

## Slide 4: Outline for Today
Last few slides on routing
How does course tie together?
Reliable Transport

## Slide 5: Distance Vector Protocol
Send distance vector based on timers:
  Every so often, send complete DV to your nbrs
  Follow “split horizon” rule:
    If use nbr for path to x, don’t send a routing entry for x to that nbr
When any values in your DV change, send updates
  Only send elements that changed
  This requires care….
Special cases:
  Poisoning a route: send ∞ when no longer have path
  Poison reverse: send ∞ to nbr you go through for path

## Slide 6
x
z
y
7
1
0
1
x
y
y
z
z
1
0
∞
Poisoned reverse
∞
Poisoning route

## Slide 7: Path-Vector
When advertise to neighbors, send them your paths
  Why might this be useful?
This prevents loops, even when not minimizing metric
  Loop prevention is now separate from routing goal
What goals might this accommodate?
  Policy choices

## Slide 8: What Might Go Wrong with PV?
Every router can make its own decisions about:
  Which of its nbrs paths to use (if any)
  Which of its paths to tell each nbr (if any)
What could go wrong with such an algorithm?
Go talk to your friends for a few minutes
  Then I’ll ask for volunteers

## Slide 9: Possible Issues
Lack of connectivity:
  If Berkeley refuses to use routes from Stanford, might not be able to reach some places in the Internet.
Lack of convergence:
  The routing algorithm is not guaranteed to converge.
  Will discuss this when we get to interdomain routing…

## Slide 10: Fundamental Tenet of Routing
Global routing state is valid if and only if:
  There are no dead ends (other than destination)*
  There are no loops
*If packet is replicated, at least one copy does not hit a dead-end.

## Slide 11: The End…
…of routing.

## Slide 12: How Does Course Tie Together?
Context (History, Goals, Principles, etc.)
Fundamental Challenges (Routing, Reliable Trans.)
Today’s Internet
  Basics (IP, TCP, Congestion Control, DNS, BGP, etc)
  Special topics (Datacenters, etc.)
How Can We Do Better?
  SDN, Naming, Routing, …
History, philosophy, BS
Conceptual Foundations
Concrete Designs
Speculative Designs

## Slide 13: Two Pedagogical Approaches
Understand how given algorithm works (textbook)
Understand the space of possible algorithms
  …and why we made the choices we did
The first: you understand how the Internet works
  And get a job at Cisco…
The second: you could design the next Internet
  Or start the next Cisco...
The second is what we do at Berkeley!
Notes: Which do you want??

## Slide 14: Purpose of Today
Understand reliable transport conceptually
  What are the fundamental aspects of reliable transport?
The goal is not to understand TCP
  TCP involves lots of detailed mechanisms, covered later
Ground rules for discussion:
  No mention of TCP
  No mention of detailed practical issues
  Focus only on “ideal” world of packets and links
Notes: Which do you want??

## Slide 15: You Must Think For Yourself
Today’s lecture requires you to engage
  How would I design a reliable service?
I will ask questions, want you to think about them
  If you think you already know this, you are wrong
  If you think you don’t know enough, you are wrong
The key to this course is focusing on fundamentals
  Yes, you will have to know some details
  But those are easy once you get the basic concepts
Two life lessons: focus on fundamentals
  And lack of familiarity is no barrier to fundamentals

## Slide 16: Decisions and Their Principles
How to break system into modules
  Dictated by Layering
Where modules are implemented
  Dictated by End-to-End Principle
Where state is stored
  Dictated by Fate-Sharing

## Slide 17: Today We Design Reliable Delivery
The end-to-end principle tells us?
  Put reliability in the end hosts, not in the network
Layering dictates putting reliability in what layer?
  In L4, above the networking layer
Fate sharing tells us?
  Keep all reliability state in ends, not in network

## Slide 18: Best Effort Service (L3)
Packets can be lost
Packets can be corrupted
Packets can be reordered
Packets can be delayed
Packets can be duplicated
….
How can you possibly make anything work with such a service model?

## Slide 19: Making Best Effort Work
Engineer network so that average case is decent
  No guarantees, but you must try….
Engineer apps so they can tolerate the worst case
  They don’t have to thrive, they just can’t die
A classical case of architecting for flexibility
  And then engineering for performance
Internet enabled app innovation and competition
  Only the hardy survived, and doomsayers were ignored

## Slide 20: Reliable Transport Is Necessary
Some app semantics involve reliable transport
  E.g., file transfer
How can we build a reliable transport service on top of an arbitrarily unreliable packet delivery?
A central challenge in bridging the gap between
  the abstractions application designers want
  the abstractions networks can easily support
Notes: But doesn’t this contradict all I’ve been saying about applications not needing functionality.
Why didn’t YOU point this out?

## Slide 21: Important Distinctions
Functionality implemented in network
  Keep minimal (easy to build, broadly applicable)
Functionality implemented in the application
  Keep minimal (easy to write)
  Restricted to application-specific functionality
Functionality implemented in the “network stack”
  The shared networking code on the host
  This relieves burden from both app and network
  This is where reliability belongs
Notes: So when I say an app needs reliable service, I mean that the app wants to offer the user that serivice.
It is one thing to say uses want relaibliity, another to say the network must provide it!

## Slide 22: Two Different Statements
Some applications need reliable service
  This means that the application writers should be able to assume this, to make their job easier
The network must provide reliable service
  This contends that end hosts cannot implement this functionality, so the network must provide it
Today we are making the first statement, and refuting the second…
  And this simple observation is what the advocates of reliable networks (as in telephony) never understood
  Why not?

## Slide 23: Challenge for Today
Building a stack that supports reliable transfer
  So that individual applications don’t need to deal with packet losses, etc.

## Slide 24: Fundamental Systems Question
How to build reliable services over unreliable components
  File systems, databases, etc.
Reliable transport is the simplest example of this

## Slide 25: Four Goals For Reliable Transfer
Correctness
Timeliness
  Minimize time until data is transferred
Efficiency
  Would like to minimize use of bandwidth
  i.e., don’t send too many packets
“Fairness”
  How well does it play with others?

## Slide 26: Start with transfer of a single packet
We can later worry about larger files, but in the beginning it is cleaner to focus on this simple case

## Slide 27: Correctness Condition?
Routing had a clean correctness condition.
We want same kind of “if and only if” characterization of “correct” reliable transport designs.
Note: this is whether the design is correct, not whether it always gives good performance.
Obvious condition: Packet is delivered to receiver.
  i.e., transport is reliable if and only if packets are always delivered to the receiver….

## Slide 28: WRONG!
What if network is partitioned?
We can’t claim a transport design is incorrect if it doesn’t work in a partitioned network!

## Slide 29: Correctness Condition?
Packet is delivered to receiver if and only if it was possible to deliver packet.

## Slide 30: WRONG!
If the network is only available at one instant of time, only an Oracle would know when to send.
We can’t claim a transport design is incorrect if it doesn’t know the unknowable…
So we need to focus on what the transport design is trying to do, not what it actually accomplishes

## Slide 31: Correctness Condition?
Resend packet if and only if the previous transmission was lost or corrupted
This is better because it refers to what the design does (which it can control), not whether it always succeeds (which it can’t)

## Slide 32: WRONG!
Impossible
  “Coordinated Attack” over an unreliable network
Consider two cases:
  Packet delivered; all packets from receiver are dropped
  Packet dropped; all packets from receiver are dropped
They are indistinguishable to sender
  In both cases, packet was sent, and no feedback at all
  Does it resend, or not?

## Slide 33: Correctness Condition?
Packet is always resent if the previous transmission was lost or corrupted.
Packet may be resent at other times.
Note:
  This invariant gives us a simple criterion for deciding if an implementation is correct
  Efficiency and timeliness are separate criteria….

## Slide 34: Complete Correctness Condition
A transport mechanism is “reliable” if and only if it resends all dropped or corrupted packets.
Sufficient (“if”): algorithm will always keep trying to deliver undelivered packets
Necessary (“only if”): if it ever lets a packet go undelivered without trying again, it isn’t reliable
Note: a transport mechanism can “give up”, but must announce this to application
  And can never falsely claim to have delivered a packet

## Slide 35: We have correctness condition
How do we achieve it?
First let’s deal with the issue of packet corruption

## Slide 36: Two Choices for Corruption
Have applications do integrity check
  Ignore it in transport protocol
Do per-packet checksum
  Won’t be perfectly reliable, still have app-level check
  So why do it? What does the E2E principle say?
This is all implemented in the ends!
  But E2E reasoning about correctness still applies
Today, we will ignore corruption, treat it as loss

## Slide 37: Back to Correctness Condition
How do we achieve it?

## Slide 38: Solution v1
Send every packet as often and fast as you can….
Definitely correct
Optimal timeliness
Infinitely bad efficiency

## Slide 39: What’s Missing?
Feedback from receiver!
If receiver does not respond, no way for sender to tell when to stop resending.
  Cannot achieve efficiency + correctness w/out feedback.

## Slide 40: Forms of Feedback
ACK: Yes, I got the packet
NACK: No, I did not get the packet
When is NACK a natural idea?
  Corruption (I got packet #5 but it was corrupted)
Ignore NACKs for rest of lecture….

## Slide 41: Solution v2
Resend packet until you get an ACK
  And receiver resends ACKs until data flow stops
Optimal timeliness
Efficiency: how much bandwidth is wasted?
  ~ B x RTT (actually 2B x RTT because of ACKs)
  ok for short latencies
  bad for long latencies

## Slide 42: Solution v3
Send packet
  Set a timer
When receiver gets packet, sends ACK
If sender receives ACK: done
If no ACK by time timer expires, resend.
Timeliness would argue for small timeout
Efficiency would argue for larger timeout
  May want to increase timer each time you try
  May want to cap the number of retries
Problems with this design?

## Slide 43: Have “solved” the single packet case
Send packet
Set timer
If no ACK when timer goes off, resend packet
  And reset timer
Tradeoff between timeliness and efficiency in the selection of timeout values:
  Too small: unnecessary retransmissions
  Too large: timeliness suffers

## Slide 44: Multiple Packets
Service Model: reliable stream of packets
  Hand up contiguous block of packets to application
Why not use single-packet solution?
  Only one packet in flight at any time
  Effective throughput: PacketSize/RTT
Use window-based approach
  Allow for W packets in-flight at any time (unack’ed)
  Sliding Window implies W packets are contiguous
    Makes sense if window is related to receiver buffer (later)

## Slide 45: Window-based Algorithms
See textbook or the web for animations….
Very simple concept:
  Send W packets
  When one gets ACK’ed, send the next packet in line
Will consider several variations….
  But first….

## Slide 46: How big should the window be?
Windows serve three purposes
  Taking advantage of the bandwidth on the link
  Limiting the bandwidth used (congestion control)
  Limiting the amount of buffering needed at the receiver
If we ignore all but the first goal, then we want to keep the sender always sending (in the ideal case)
  RTT: from sending first packet until receive first ACK
  Condition: RTT x B ~ W x Packet Size

## Slide 47: RTT x B ~ W x Packet Size
Recall the Bandwidth-Delay Product (BDP)
BDP = bandwidth × propagation delay
B x RTT is merely 2 x BDP
Window sizing rule: Total bits in flight is roughly amount that fits into forward and reverse “pipes”
  Here pipe is complete path, not single link…
  This is not a “detail”, this is a fundamental concept….
bandwidth
Propagation delay
delay x bandwidth

## Slide 48: Where Are We?
Figured out correctness condition:
  Always resend lost/corrupted packets
Figured out single packet case:
  Send packet, set timer, resend if no ACK when timer expires
Multiple packets
  Allow many packets (W) be in flight at once
  And know what the ideal window size W is
    RTTxB/PacketSize
What’s left to design?

## Slide 49: Three Design Considerations
Nature of feedback
  What should ACKs tell us when we have many packets in flight?
Detection of loss
Response to loss

## Slide 50: Possible Feedback From Receiver
Ideas?

## Slide 51: ACK Individual Packets
Strengths:
  Know fate of each packet
  Impervious to reordering
  Simple window algorithm
    W independent single-packet algorithms
    When one finishes, grab next packet
Weaknesses?
  Loss of ACK packet requires a retransmission

## Slide 52: Cumulative ACK
ACK the highest sequence number for which all previous packets have been received
  Implementations often send back “next expected packet”, but that’s just a detail
Strengths:
  Recovers from lost ACKs
Weaknesses?
  Confused by reordering
  Incomplete information about which packets have arrived

## Slide 53: Full Information Feedback
List all packets that have been received
  Give highest cumulative ACK plus any additional packets
  Feasible if only small holes
Strengths:
  As much information as you could hope for
  Resilient form of individual ACKs
Weaknesses?
  Could require sizable overhead in bad cases

## Slide 54: Detecting Loss
If packet times out, assume it is lost….
How else can you detect loss?

## Slide 55: Loss with individual ACKs
Assume packet 5 is lost, but no others
Stream of ACKs will be:
  1
  2
  3
  4
  6
  7
  8
  ….

## Slide 56: Loss with individual ACKs
Could resend packet when k “subsequent packets” are received
Response to loss:
  Resend missing packet
  Continue window based protocol

## Slide 57: Loss with full information
Same story, except that the “hole” is explicit
Stream of ACKs will be:
  Up to 1
  Up to 2
  Up to 3
  Up to 4
  Up to 4, plus 6
  Up to 4, plus 6,7
  Up to 4, plus 6,7,8
  ….

## Slide 58: Loss with full information
Could resend packet when k “subsequent packets” are received
Response to loss:
  Resend missing packet
  Continue window based protocol

## Slide 59: Loss with cumulative ACKs
Assume packet 5 is lost, but no others
Stream of ACKs will be:
  1
  2
  3
  4
  4 (sent when packet 6 arrives)
  4 (sent when packet 7 arrives)
  4 (sent when packet 8 arrives)
  ….

## Slide 60: Loss with cumulative ACKs (cont’d)
“Duplicate ACKs” are a sign of an isolated loss
  The lack of ACK progress means 5 hasn’t been delivered
  Stream of ACKs means some packets are being delivered
Therefore, could trigger resend upon receiving k duplicate ACKs
But response to loss is trickier….

## Slide 61: Loss with cumulative ACKs (cont’d2)
Two choices:
  Send missing packet and optimistically assume that subsequent packets have arrived
    i.e., increase W by the number of Dup ACKs
  Send missing packet, and wait for ACK
Timeout-detected losses also problematic
  If packet 5 times out, packet 6 is about to time out also
  Do you resend both?
  Do you resend 5 and wait?
  ….

## Slide 62: Go-Back-N
Simple algorithm (not advisable, but simple)
Sliding window (only W contiguous packets)
When a loss is detected by timeout, resend all W packets starting with loss
Receiver discards out-of-order packets
This is one possible approach, will discuss others when we get to TCP….

## Slide 63: All the bad things best effort can do…
Packets can be lost
Packets can be corrupted
Packets can be reordered
Packets can be delayed
Packets can be duplicated

## Slide 64: Effect of Reordering?
Individual ACKs: not a problem
Full information: not a problem
Cumulative ACKs: create Dup ACKs
  Why is this a problem?

## Slide 65: Effect of Long Delays?
Possible timeouts (for all designs)

## Slide 66: Effect of Duplication?
Produce Duplicate ACKs
  Could be confused for loss with cumulative ACKs
  But duplication is rare….

## Slide 67: Possible Design for Reliable Trans.
Full information ACKs
Window-based, with retransmissions after:
  Timeout
  K subsequent ACKs
This is correct, timely, efficient

## Slide 68: Fairness? (come back to later)
Adjust W based on losses….
In a way that flows receive same shares
Short version:
  Loss: cut W by 2
  Successful receipt of window: W increased by 1

## Slide 69: Overview of Reliable Transport
Window-based flow control separates concerns
  Size of W:
  Nature of feedback:
  Response to loss:
Can design each aspect relatively independently
Can be correct, efficient, timely, and fair

## Slide 70: Many Implementation Choices
Feedback from receiver: ACKs vs NACKs
  Can NACKs alone achieve “correctness”?
  Can ACKs alone achieve “correctness”?
Variations on ACKs
  Full information
  Individual packets
  Cumulative (TCP)
When to resend
  Timeout
  Duplicate ACKs
  NACKs

## Slide 71: Implementation Choices
These implementation choices affect:
  Timeliness
  Efficiency
  Fairness
  ….
These are important concerns
  but correctness is more fundamental
Design must start with correctness
  Can then “engineer” its performance with various hacks
  These hacks can be “fun” but don’t let them distract you

## Slide 72: Are We Done?
There are other approaches….
Suggestions?

## Slide 73: Alternate Strategy: Rateless Codes
Use special encoding
  Receipt of any set of M packets allows you to recover file
  Where M is close to the size of the original file
Receiver only sends ACK when M are received
  Sender keeps sending until receives ACK
Timely, Correct
  How efficient is it?
  It wastes BxRTT on every flow. Isn’t that awful?

## Slide 74: The Paradox of Internet Traffic
The majority of flows are short
  A few packets
The majority of bytes are in long flows
  MB or more
And this trend is accelerating…

## Slide 75: Inefficiency
The wasted bandwidth ~ BxRTT
For long flows, this is small compared to total file
For short flows, this is large compared to file
  But most of the bandwidth is in long flows!
This is not a terrible idea

## Slide 76: What Have We Done Today?
Gone from first principles
  Correctness condition for reliable transport
…to design for single packets…
...to design for multiple packets...
  Very close to modern TCP
...to radically different designs
  Which could replace TCP
All done by you, in 80 minutes.

## Slide 77: Next Lecture
End of fundamentals!
Design of IP