## Slide 1: CS 168 Interdomain Routing (the good, the bad, and the ugly)
Fall 2016
Scott Shenker
CS168.io
http://inst.eecs.berkeley.edu/~cs168/fa16/

## Slide 2
Ssssshhhhhhhhhhhhhhh

## Slide 3: Announcements
Fill out survey! Due tomorrow….
171 people have registered their participation
  Come see me during office hours, or ask a question
  You only have a few weeks left!
Plan for rest of semester: 7 more lectures
  Interdomain routing (this and next lecture)
  Routing research and multicast
  Datacenters (Kay)
  SDN, NFV, security, and other topics (two lectures)
  Rethinking Internet
  Final lecture

## Slide 4: Rules of Engagement
BGP is confusing, but not deep.
Ask questions if you are confused, or yell “help!”
I have limited myself to 70 slides today to make time for clarifying questions….

## Slide 5: Outline
Background for interdomain routing
BGP: Key ideas
BGP: Common policies
BGP: Protocol details
BGP: Issues (next time)

## Slide 6: Background for Interdomain Routing
What? Why? When?

## Slide 7: L3 Routing
Provides paths between networks (i.e., subnets)
  Prefixes refer to the “network” portion of the address
So far, only considered routing within a domain
  All routers have same routing metric (shortest path)
Many issues (goals, incentives, etc.) can be ignored because there is central administrative control over routers
But we can’t ignore those issues any more!

## Slide 8: Internet more than a single domain…
Internet not just unstructured collection of networks
  “Networks” in the sense of subnets
Internet is comprised of “autonomous systems”
  Independently run networks, some are commercial ISPs
  Currently over 50,000 Ases
  Think AT&T, France Telecom, UCB, IBM, Intel, etc.
ASes are sometimes called “domains”
  Hence “interdomain routing”
Each AS is assigned a unique identifier
  16 bit AS Number (ASN); E.g., ASN 25 is UCB

## Slide 9: Internet Comprised of Many ASes
Large ISP
Large ISP
Dial-Up
ISP
Access
Network
Small ISP
Stub
Stub
Stub
Notes: Stub AS
Multihomed AS
Trnsit AS

## Slide 10
“Interior Routers”
“Autonomous System (AS)” or “Domain” Region of a network under a single administrative entity
“Border Routers”
An “end-to-end” route

## Slide 11: Common Kinds of ASes
Stub: An AS that merely sends/receives packets on behalf of its users.
  Companies, Universities, etc.
Transit: carries packets on behalf of other ASes.
  Typically one of three “tiers”
Tier 1: global ISPs, don’t buy service from other ISPs
Tier 2: regional ISPs, typically buy service from tier 1
Tier 3: local ISPs, buy service from tier 1 or 2

## Slide 12: Hold on….
You’ve talked about so many routing algorithms
  Distance vector
  Link state
  Learning switches
  Spanning trees
  Path vector
  …..
How do they fit together?

## Slide 13: Three levels in routing hierarchy
L2: Within single subnet: to reach individual hosts
  Learning switches; based on MAC addresses
Intradomain: routes between networks (L3)
  Distance Vector, Link State: based on IP addresses
Interdomain: routes between ASes (L3)
  Today’s lecture
Need a protocol to route between domains
  BGP is current standard: based on IP addresses
Aside: using IP addresses for both intradomain
and interdomain routing is Internet’s biggest mistake

## Slide 14: The Rise of a New Routing Paradigm
The idea of routing through networks was well-known before the Internet
  Dijkstra's algorithm 1956 (shortest path on graph)
  Bellman-Ford 1958 (distributed shortest path algorithm)
  All designed to find “least cost” paths
The notion of “autonomous systems” which could implement their own private policies was new
  BGP was hastily designed in response to this need
  Developed 1989-1995
It has mystified us ever since…..
  Initially ignored by research community, then subject of a flurry of papers exploring its many mysteries….

## Slide 15: Administrative Preferences shape Interdomain routing (IDR)
ASes want freedom to pick routes based on policy
  “My traffic can’t be carried over my competitor’s network”
  “I don’t want to carry that AS’s traffic through my network”
  Not expressible as Internet-wide “least cost”!
    All old routing paradigms useless…..
ASes want autonomy
  Want to choose their own internal routing protocol
  Want to choose their own external policy
ASes want privacy
  Don’t want to announce these choices to others

## Slide 16: Interdomain Routing Requirements
Policy is what IDR must support
Autonomy and privacy is how it must be supported
BGP might seem like a very unnatural design
  But is the only reasonable solution to these requirements!

## Slide 17: Any Questions?

## Slide 18: Two Questions
What drives these policies? Why not just use shortest paths?
How do we support them, while providing autonomy and privacy?

## Slide 19: Topology and policy is shaped by the business relationships between ASes
ASes connect only if they have business relationship
Two basic kinds of relationships between ASes
  Customer-provider: AS B carries AS A’s traffic, for a fee
    B is A’s provider, A is B’s customer
  Peers: AS A and B carry each other’s traffic, for free
Money flow
  Customer pays provider
  Peers don’t pay each other
    Exchange roughly equal traffic
Notes: Ehy???

## Slide 20: Business Relationships
peer
peer
provider
customer
Relations between ASes
Customers pay provider
Peers don’t pay each other
Business Implications

## Slide 21: Why peer?
peer
peer
provider
customer
Relations between ASes
Customers pay provider
Peers don’t pay each other
Business Implications
A
B
C
D
E
E.g., D and E talk a lot
Peering saves B and C money
Why don’t D
and E peer directly?

## Slide 22: Two Principles For Typical Policies
#1: Don’t carry traffic if you are not being paid!
That means traffic either comes from customer
  Or is going to a customer
#2: Save/make money when sending traffic
This means don’t send to provider if you have choice
Remember these, and everything makes sense!

## Slide 23: Routing Follows the Money!
ASes provide “transit” between their customers
Peers do not provide transit between other peers
traffic allowed
traffic not allowed
A
B
C
D
E
F
Q
Pr
Cu
Peer
Peer
Notes: What about through Q??

## Slide 24: Routing Follows the Money!
Routes are “valley free” (we return to this later)
F does not carry traffic for which:
  It has to pay both A and C
  And does not satisfy any of its own customers
C
F
Pr
Cu
Peer
Peer
A

## Slide 25: Tier 1 and Typical Policies
All Tier 1 providers peer with each other
  (mostly true)
They form a fully-connected core of the Internet
Policy-based routing only works because:
  Policies follow basic money rule (discussed more later)
  Tier 1 a full mesh
Otherwise, policy-based routing could have connectivity and convergence problems
  to be discussed…

## Slide 26: In Short
AS topology reflects business relationships between ASes
Business relationships between ASes impact which routes are acceptable
IDR design must support these policy choices
  Allowing domains autonomy and privacy
Border Gateway Protocol (BGP) is current design

## Slide 27: Any Questions?

## Slide 28: Border Gateway Protocol (BGP)
Key Ideas

## Slide 29: Interdomain Routing: Setup
Destinations are IP prefixes (12.0.0.0/8)
  Prefix residing in some domain
Nodes are Autonomous Systems (ASes)
  Internals of each AS are hidden
Link represent presence of both physical/virtual link and business relationship
BGP is implemented by AS border routers

## Slide 30: BGP: Basic Idea
Each AS selects the “best” route it hears advertised for a prefix
An AS advertises (“exports”) its best routes to one or more IP prefixes
You’ve heard this story before!
Notes: Arrows are routing message

## Slide 31: BGP inspired by Distance Vector
Per-destination route advertisements
No global sharing of network topology information
  Why not use link-state approach?
Iterative and distributed convergence on paths
With four crucial differences!

## Slide 32: The Four Differences from Classic DV
Not required to pick “shortest path”
  Can make choices consistent with policy
  And these choices are autonomous and private
But then must find another way to avoid loops
  Use Path Vector (already discussed)
Selective route advertisements
  Another aspect of policy
  Done autonomously and privately
Route aggregation (already discussed...)

## Slide 33: Differences between BGP and DV (1) not picking shortest path routes
BGP selects the best route based on policy, not shortest distance (least cost)
How do we avoid loops?
2
3
1
Node 2 may prefer “2, 3, 1” over “2, 1”

## Slide 34: Differences between BGP and DV (2) path-vector routing
Key idea: advertise the entire path
  Distance vector: send distance metric per dest d
  Path vector: send the entire path for each dest d
3
2
1
d
“d: path (2,1)”
“d: path (1)”
data traffic
data traffic

## Slide 35: Differences between BGP and DV (2) path-vector routing
Key idea: advertise the entire path
  Distance vector: send distance metric per destination
  Path vector: send the entire path for each destination
Benefits
  loop avoidance is easy

## Slide 36: Loop Detection w/ Path-Vector
Node can easily detect a loop
  Look for its own node identifier in the path
Node can simply discard paths with loops
  E.g., node 1 sees itself in the path “3, 2, 1”
  E.g., node 1 simply discards the advertisement
3
2
1
“d: path (2,1)”
“d: path (1)”
“d: path (3,2,1)”
d

## Slide 37: Differences between BGP and DV (2) path-vector routing
Key idea: advertise the entire path
  Distance vector: send distance metric per destination
  Path vector: send the entire path for each destination
Benefits
  loop avoidance is easy
  flexible policies based on entire path
    E.g., avoid certain countries or providers

## Slide 38: Differences between BGP and DV (3) Selective route advertisement
For policy reasons, an AS may choose not to advertise a route to a destination
Hence, reachability is not guaranteed even if graph is connected
AS 2
AS 3
AS 1
Example: AS#2 does not want to carry traffic between AS#1 and AS#3

## Slide 39: Differences between BGP and DV (4) BGP may aggregate routes
For scalability, BGP may aggregate routes for different prefixes
AT&T a.0.0.0/8
LBL a.b.0.0/16
UCB a.c.0.0/16
a.*.*.* is this way
foo.com a.d.0.0/16

## Slide 40: Ingredients of BGP
Start with two things we know about:
  Path-vector (needed for loop-freeness)
  Aggregation (needed for scaling)
Introduce two new concepts:
  General path selection (based on arbitrary criteria)
  General path advertisement (based on arbitrary criteria)
All four are needed to make BGP work
  The first two are straightforward
  But the latter two can make your head spin…

## Slide 41: Policy imposed in how routes are selected and exported
Selection: Which path to use?
  controls whether/how traffic leaves the network
Export: Which path to advertise?
  controls whether/how traffic enters the network
Can reach 128.3/16
blah blah
Route selection
Customer
Competitor
1
5
10
Route export
Notes: Arrows: routing messages!

## Slide 42: Two Crucial Points
Selection: Which path to use?
  Determines where your traffic goes
  Why? Because this involves choosing the route….
Export: Which path to advertise?
  Determines which traffic you carry
  Why? This determines who can send traffic to you

## Slide 43: Border Gateway Protocol (BGP)
Common Policies

## Slide 44: Typical Selection Policy
In decreasing order of priority
  make/save money (send to customer > peer > provider)
  maximize performance (smallest AS path length?)
  minimize use of my network bandwidth (“hot potato”)
  …
  …
Most important rule:
  Favor customers over peers….
  ….and peers over providers

## Slide 45: Typical Export Policy
Destination prefix advertised by… | Export route to…
Customer | Everyone (providers, peers, other customers)
Peer | Customers
Provider | Customers
We’ll refer to these as the “Gao-Rexford” rules
(capture common -- but not required! -- practice!)
Notice that ”Customer” shows up
on one side or another!

## Slide 46: Gao-Rexford
peers
providers
customers
With Gao-Rexford, the AS policy graph is a DAG (directed acyclic graph) and routes are “valley free”

## Slide 47: Any Questions?

## Slide 48: Border Gateway Protocol (BGP)
Protocol Details (zzzzzzz….)

## Slide 49: Who speaks BGP?
Border router
Internal router
Border routers at an Autonomous System
Notes: Say “There are four parts to internet routing” (don’t say in route selection)

## Slide 50: Some Border Routers Don’t Need BGP
Customer that connects to a single upstream ISP
  The ISP can advertise prefixes into BGP on behalf of customer
  … and the customer can simply default-route to the ISP
Provider
Customer
Install default routes pointing to Provider
Install routes 130.132.0.0/16 pointing to Customer
130.132.0.0/16

## Slide 51: What does “speak BGP” mean?
Implement the BGP protocol standard
  read more here: http://tools.ietf.org/html/rfc4271
Specifies messaging with other BGP “speakers”
  message types (e.g., route advertisements, updates)
  message syntax
And how to process these messages
  e.g., “when you receive a BGP update, do…. “
  Follows BGP state machine
  Protocol spec + policy decisions, etc.

## Slide 52: BGP “sessions”
A border router speaks BGP with border routers in other ASes
“eBGP session”
Notes: Say “There are four parts to internet routing” (don’t say in route selection)

## Slide 53: BGP “sessions”
A border router speaks BGP with other (interior and border) routers in its own AS
“iBGP session”
Notes: Say “There are four parts to internet routing” (don’t say in route selection)

## Slide 54: eBGP, iBGP, IGP
eBGP: BGP sessions between border routers in different ASes
  Learn routes to external destinations
iBGP: BGP sessions between border routers and other routers within the same AS
  distribute externally learned routes internally
IGP: “Interior Gateway Protocol” = Intradomain routing protocol
  provide internal reachability
  e.g., OSPF, RIP

## Slide 55: Putting the pieces together
Provide internal reachability (IGP)
Learn routes to external destinations (eBGP)
Distribute externally learned routes internally (iBGP)
Travel shortest path to egress (IGP)
6
2
4
9
2
1
3
3

## Slide 56: If this isn’t clear, don’t worry….
Every router in AS has two routing tables:
  From IGP: next hop to all internal locations
  From iBGP: egress router to all external locations
For internal addresses, just use IGP
  Entry <internal subnet, internal next hop>
For external locations:
  Use IGP to find next hop to egress router
  Entry <external prefix, internal next hop>

## Slide 57: Basic Messages in BGP
Open
  Establishes BGP session
  BGP uses TCP
Notification
  Report unusual conditions
Update
  Inform neighbor of new routes
  Inform neighbor of old routes that become inactive
Keepalive
  Inform neighbor that connection is still viable

## Slide 58: Route Updates
Format <IP prefix: route attributes>
  attributes describe properties of the route
Two kinds of updates
  announcements: new routes or changes to existing routes
  withdrawal: remove routes that no longer exist

## Slide 59: Route Attributes
Routes are described using attributes
  Used in route selection/export decisions
Some attributes are local
  i.e., private within an AS, not included in announcements
Some attributes are propagated with eBGP route announcements
There are many standardized attributes in BGP
  We will discuss a few

## Slide 60: Attributes (1): ASPATH
Carried in route announcements
Vector that lists all the ASes a route advertisement has traversed (in reverse order)
AS 7018
AT&T
AS 12654
128.112.0.0/16
AS path = 7018 88
AS 88
Princeton, 128.112/16
IP prefix = 128.112.0.0/16
AS path = 88

## Slide 61: Attributes (2): LOCAL PREF
“Local Preference”
Used to choose between different AS paths
The higher the value the more preferred
Local to an AS; carried only in iBGP messages
AS4
AS2
AS3
AS1
140.20.1.0/24
BGP table at AS4:
Notes: Because communicated to all IBGP routers within AS, all routers have a common view of how to exit the AS.
This differs from MED in 2 ways: (1) the destination prefix can be anywhere in the internet, not just in the next AS (as in the case for MED). (2) the AS that sets Local_Pref, is also the one that uses it. This allows one node to tell everyone locally what the best way out is.
MED can’t be used in this example because there is exactly one connection between any pair of AS’s.

## Slide 62: Example: iBGP and LOCAL PREF
Both routers prefer the path through AS 2 on the left
I-BGP
AS 4
AS 3
Local Pref = 100
Local Pref = 90
AS 2
AS1

## Slide 63: Attributes (3) : MED
“Multi-Exit Discriminator”
Used when ASes are interconnected via 2 or more links to specify how close a prefix is to the link it is announced on
Lower is better
AS announcing prefix sets MED
AS receiving prefix (optionally!) uses MED to select link
Link B
Link A
MED=10
MED=50
AS1
AS2
AS3
destination prefix

## Slide 64: Attributes (4): IGP cost
Used for hot-potato routing
  Each router selects the closest egress point based on the path cost in intra-domain protocol
hot potato
A
B
C
D
G
E
F
4
5
3
9
3
4
10
8
8
A
B
dst

## Slide 65: IGP may conflict with MED
Dsf
A
B
MED=100
MED=500

## Slide 66: Typical Selection Policy
In decreasing order of priority
  make/save money (send to customer > peer > provider)
  maximize performance (smallest AS path length)
  minimize use of my network bandwidth (“hot potato”)
  …
  …

## Slide 67: Using Attributes
Rules for route selection in priority order
Priority | Rule | Remarks
1 | LOCAL PREF | Pick highest LOCAL PREF
2 | ASPATH | Pick shortest ASPATH length
3 | MED | Lowest MED preferred
4 | eBGP > iBGP | Did AS learn route via eBGP (preferred) or iBGP?
5 | iBGP path | Lowest IGP cost to next hop (egress router)
6 | Router ID | Smallest next-hop router’s IP address as tie-breaker

## Slide 68: BGP UPDATE Processing
Best Route
Selection
Apply Import
Policies
Best Route
Table
Apply Export
Policies
forwarding
Entries
BGP
Updates
BGP
Updates
IP Forwarding Table
Open ended programming.
Constrained only by vendor configuration language
Data plane
Control plane
Data packets
Data packets

## Slide 69: Border Gateway Protocol (BGP)
Issues with BGP

## Slide 70: Issues with BGP
Reachability
Security
Convergence
Performance
Anomalies
Relevance