## Slide 1: CS 168 Interdomain Routing (II)
Fall 2016
Scott Shenker
CS168.io
http://inst.eecs.berkeley.edu/~cs168/fa16/

## Slide 2
Ssssshhhhhhhhhhhhhhh

## Slide 3: “A republic, if you can keep it.”
The future of our country rests in your hands…
Elections matter, policies matter, values matter
They say the arc of history bends towards justice...
But in the last year we have relegitimized hate, intolerance, bigotry, and voting restrictions
This fight will not end today; it is your fight to win
  Increase your voting rate, and the game is over.

## Slide 4: CS194: Practical Networking
T/Th 12:30-2:00pm in Soda 420
  Will send application link
Two projects and a reading period
Project 1: Network measurement and security
  Nick Weaver
Project 2: Software-Defined Networking
  Murphy McCauley (and me)
Reading class: 3 or 4 weeks (mini 268)
  Me

## Slide 5: Announcements
HW4 is out.
Thank you for the course feedback!

## Slide 6: Lessons from Feedback
My TAs are great (indeed, “flawless”)
We have many things to improve on
  Thanks for the suggestions!
I can’t please everyone….
  Too fast vs too slow
  Hate lecturing style vs not
  One 3 hour lecture vs 3 one-hour lectures
  ...
I am old and out of touch....

## Slide 7: I am a conservative….
“A person who is averse to change and holds to traditional values and attitudes….”
My experience is from a different era and ethos
  Go to class, take careful notes, ask questions in real-time
One thread of comments suggests steps that make it easier to take class offline
  Webcasting (a huge favorite)
  Various ways to turn lecture slides into better class notes
  ...
This is not how I teach, or why I teach….
  Want to influence how you think more than what you know
  And that requires engagement, not better lecture notes

## Slide 8: But I might be wrong….
So after the semester, come tell me why these steps would not turn the class into a wasteland of empty seats….
There’s a fundamental question here. Does optimizing for your time and convenience lead to the best educational experience?
I say no, but I’m willing to be convinced otherwise....

## Slide 9: Participation
202 people have registered their participation
279 students need to participate
  4 office hours remaining
  7 classes (including today) remaining
You do the math...
  Over 25 people per opportunity. Not going to happen.
No excuses accepted. Do it now…..

## Slide 10: Feedback on Participation
Some called it “silly” (or worse)
To me, if you don’t ask a question in class, or in office hours, you aren’t engaged.
And I teach to get people engaged in questions, not to have them passively absorb facts.

## Slide 11: Agenda
Quick review of BGP basics
Protocol details
Analysis of BGP “issues”

## Slide 12: Policy imposed in how routes are selected and exported
Can reach 128.3/16
blah blah
Route selection
Customer
Competitor
1
5
10
Route export
Notes: Arrows: routing messages!

## Slide 13: The Role of Selection and Export
Selection: Which path to use?
  Determines where your traffic goes
  Why? Because this involves choosing the route….
Export: Which path to advertise?
  Determines which traffic you carry
  Why? This determines who can send traffic to you

## Slide 14: Typical Selection Policy
Most important rule:
  Favor customers over peers….
  ….and peers over providers

## Slide 15: Typical Export Policy
Destination prefix advertised by… | Export route to…
Customer | Everyone (providers, peers, other customers)
Peer | Customers
Provider | Customers

## Slide 16: Customer-Provider-Peering
Peering relationships can be cyclic
  The peer of my peer can also be my peer
But we always assume that the graph of customer-provider relationships is acyclic
You cannot find a sequence of domains Ai where
  An=A1
  Ai+1 is provider of Ai for all I
This means one can arrange providers in a hierarchy (e.g., tier 1, tier 2, tier 3)

## Slide 17: Gao-Rexford: Typical Policies/Acyclic
Current practices close to the Gao-Rexford model
This is why interdomain routing works
In its full generality, BGP has many problems
But current business practices eliminate some...

## Slide 18: Reasoning about Reachability
Selection rules: never cause unreachability
  I am picking one of the available routes
  So if a route is offered, I am connected to that prefix
Export rules: can cause unreachability
  If I choose to not export some routes, then an AS might never be able to reach those prefixes
If the graph is connected, but an AS cannot reach a given prefix, it is because of export rules….

## Slide 19: Gao-Rexford Interesting Fact #1
Adding IDR links cannot hurt reachability
  If A could reach B before, then they still can after addition
  Reason: new link changes selection, not export
    I continue to export all routes I previously exported
Destination prefix advertised by… | Export route to…
Customer | Everyone (providers, peers, other customers)
Peer | Customers
Provider | Customers

## Slide 20: Gao-Rexford Interesting Fact #2
Paths are “single-peaked”.
Following sequence of domains from source to destination, you will find:
  Np provider links, where Np≥0
  0 or 1 peering links
  Nc customer links, where Nc≥0
That is, paths go up provider hierarchy, and then down….with perhaps a peering link at top.

## Slide 21: Routing Follows the Money!
Can D reach F?
traffic allowed
traffic not allowed
A
B
C
D
E
F
Q
Pr
Cu
Peer
Peer
Notes: What about through Q??

## Slide 22: eBGP, iBGP, IGP
eBGP: BGP sessions between border routers in different ASes
  Learn routes to external destinations
iBGP: BGP sessions between border routers and other routers within the same AS
  distribute externally learned routes internally
IGP: “Interior Gateway Protocol” = Intradomain routing protocol
  provide internal reachability
  e.g., OSPF, RIP

## Slide 23: Short Summary
Every router in AS has two routing tables:
  From IGP: next hop to all internal locations
  From iBGP: egress router to all external locations
For internal addresses, just use IGP
  Entry <internal subnet, internal next hop>
For external locations:
  Use IGP to find next hop to egress router
  Entry <external prefix, internal next hop>

## Slide 24: In Reality….
Many different ways to configure a domain
Option #1: run iBGP between all routers in domain
  Requires N2 connections. Not always practical.
  This is what we will assume.
Option #2: only run iBGP between border routers
  Inject external routes into IGP
  Can impair functioning of IGP due to scaling
Option #3: Run a route reflector for iBGP
  N rather than N2 connections
  Can also use “BGP confederations”

## Slide 25: Any Questions?

## Slide 26: Border Gateway Protocol (BGP)
Protocol Details (zzzzzzz….)

## Slide 27: Basic Messages in BGP
Open
  Establishes BGP session
  BGP uses TCP
Notification
  Report unusual conditions
Update
  Inform neighbor of new routes
  Inform neighbor of old routes that become inactive
Keepalive
  Inform neighbor that connection is still viable

## Slide 28: Route Updates
Format <IP prefix: route attributes>
  attributes describe properties of the route
Two kinds of updates
  announcements: new routes or changes to existing routes
  withdrawal: remove routes that no longer exist

## Slide 29: Route Attributes
Routes are described using attributes
  Used in route selection/export decisions
Some attributes are local
  i.e., private within an AS, not included in announcements
Some attributes are propagated with eBGP route announcements
There are many standardized attributes in BGP
  We will discuss a few

## Slide 30: Attributes (1): ASPATH
Carried in route announcements
Vector that lists all the ASes a route advertisement has traversed (in reverse order)
AS 7018
AT&T
AS 12654
128.112.0.0/16
AS path = 7018 88
AS 88
Princeton, 128.112/16
IP prefix = 128.112.0.0/16
AS path = 88

## Slide 31: Attributes (2): LOCAL PREF
“Local Preference”
Used to choose between different AS paths
The higher the value the more preferred
  This is where customer > peer > provider is expressed
Local to an AS; carried only in iBGP messages
AS4
AS2
AS3
AS1
140.20.1.0/24
BGP table at AS4:
Notes: Because communicated to all IBGP routers within AS, all routers have a common view of how to exit the AS.
This differs from MED in 2 ways: (1) the destination prefix can be anywhere in the internet, not just in the next AS (as in the case for MED). (2) the AS that sets Local_Pref, is also the one that uses it. This allows one node to tell everyone locally what the best way out is.
MED can’t be used in this example because there is exactly one connection between any pair of AS’s.

## Slide 32: Attributes (3) : MED
“Multi-Exit Discriminator”
Used when ASes are interconnected via 2 or more links to specify how close a prefix is to the link it is announced on
Lower is better
AS announcing prefix sets MED
AS receiving prefix (optionally!) uses MED to select link
Link B
Link A
MED=10
MED=50
AS1
AS2
AS3
destination prefix

## Slide 33: Attributes (4): IGP cost
Used for hot-potato routing
  Each router selects the closest egress point based on the path cost in intra-domain protocol
hot potato
A
B
C
D
G
E
F
4
5
3
9
3
4
10
8
8
A
B
dst

## Slide 34: IGP may conflict with MED
Dsf
A
B
MED=100
MED=500
Can lead to asymmetric routes!

## Slide 35: Typical Selection Policy is Ordered
In decreasing order of priority
  make/save money (send to customer > peer > provider)
  maximize performance (smallest AS path length)
  …
  …

## Slide 36: Using Attributes
Typical rules for route selection in priority order
Priority | Rule | Remarks
1 | LOCAL PREF | Pick highest LOCAL PREF
2 | ASPATH | Pick shortest ASPATH length
3 | MED | Lowest MED preferred
4 | eBGP > iBGP | Did AS learn route via eBGP (preferred) or iBGP?
5 | iBGP path | Lowest IGP cost to next hop (egress router)
6 | Router ID | Smallest next-hop router’s IP address as tie-breaker

## Slide 37: BGP UPDATE Processing
Best Route
Selection
Apply Import
Policies
Best Route
Table
Apply Export
Policies
forwarding
Entries
BGP
Updates
BGP
Updates
IP Forwarding Table
Open ended programming.
Constrained only by vendor configuration language
Data plane
Control plane
Data packets
Data packets
Import Policies:
Set attributes, etc.

## Slide 38: Border Gateway Protocol (BGP)
Issues with BGP

## Slide 39: Issues with BGP
Reachability
Security
Convergence
Performance
Anomalies
Relevance

## Slide 40: (1) Reachability
In normal routing, if graph is connected then reachability is assured
With policy routing, this does not always hold
AS 2
AS 3
AS 1
Provider
Provider
Customer

## Slide 41: Why Does the Internet Work?
Assumption 1: Policies obey Gao-Rexford
  Or at least are no more restrictive..
Assumption 2: Starting from any AS, and following the chain of providers, leads to a tier 1 ISP
  Tier 1: group of ISPs that all peer with each other
Under these assumptions, all ASes are connected
Proof?
  First, eliminate all peering except at tier 1. Reachable
  Second, recall lemma: adding links does not disconnect

## Slide 42: (2) Security
An AS can claim to serve a prefix that they actually don’t have a route to (blackholing traffic)
  Problem not specific to policy or path vector
  Important because of AS autonomy
  Fixable: make ASes “prove” they have a path
    How? What would you need?
Note: AS may forward packets along a route different from what is advertised
  Forcing the advertised paths to exist is doable
  Forcing an AS to use that path is much harder!
    Why?

## Slide 43: (3) Convergence
Result: If all AS policies follow “Gao-Rexford” rules, BGP is guaranteed to converge (safety)
For arbitrary policies, BGP may fail to converge!

## Slide 44: Example of Policy Oscillation
1
2
3
1 3 0
1 0
3 2 0
3 0
2 1 0
2 0
0
“1” prefers “1 3 0”
over “1 0” to reach “0”

## Slide 45: Step-by-Step of Policy Oscillation
Initially: nodes 1, 2, 3 know only shortest path to 0
1
2
3
1 3 0
1 0
3 2 0
3 0
2 1 0
2 0
0

## Slide 46
1 advertises its path 1 0 to 2
1
2
3
1 3 0
1 0
3 2 0
3 0
2 1 0
2 0
0
advertise: 1 0
Step-by-Step of Policy Oscillation

## Slide 47
1
2
3
1 3 0
1 0
3 2 0
3 0
2 1 0
2 0
0
Step-by-Step of Policy Oscillation

## Slide 48
1
2
3
1 3 0
1 0
3 2 0
3 0
2 1 0
2 0
0
advertise: 3 0
3 advertises its path 3 0 to 1
Step-by-Step of Policy Oscillation

## Slide 49
1
2
3
1 3 0
1 0
3 2 0
3 0
2 1 0
2 0
0
Step-by-Step of Policy Oscillation

## Slide 50
1
2
3
1 3 0
1 0
3 2 0
3 0
2 1 0
2 0
0
withdraw: 1 0
1 withdraws its path 1 0 from 2
Step-by-Step of Policy Oscillation

## Slide 51
1
2
3
1 3 0
1 0
3 2 0
3 0
2 1 0
2 0
0
Step-by-Step of Policy Oscillation

## Slide 52
1
2
3
1 3 0
1 0
3 2 0
3 0
2 1 0
2 0
0
advertise: 2 0
2 advertises its path 2 0 to 3
Step-by-Step of Policy Oscillation

## Slide 53
1
2
3
1 3 0
1 0
3 2 0
3 0
2 1 0
2 0
0
Step-by-Step of Policy Oscillation

## Slide 54
1
2
3
1 3 0
1 0
3 2 0
3 0
2 1 0
2 0
0
withdraw: 3 0
3 withdraws its path 3 0 from 1
Step-by-Step of Policy Oscillation

## Slide 55
1
2
3
1 3 0
1 0
3 2 0
3 0
2 1 0
2 0
0
Step-by-Step of Policy Oscillation

## Slide 56
1
2
3
1 3 0
1 0
3 2 0
3 0
2 1 0
2 0
0
1 advertises its path 1 0 to 2
Step-by-Step of Policy Oscillation
advertise: 1 0

## Slide 57
1
2
3
1 3 0
1 0
3 2 0
3 0
2 1 0
2 0
0
Step-by-Step of Policy Oscillation

## Slide 58
1
2
3
1 3 0
1 0
3 2 0
3 0
2 1 0
2 0
0
withdraw: 2 0
2 withdraws its path 2 0 from 3
Step-by-Step of Policy Oscillation

## Slide 59
1
2
3
1 3 0
1 0
3 2 0
3 0
2 1 0
2 0
0
We are back to where we started!
And there is no stable state…..
Step-by-Step of Policy Oscillation

## Slide 60: How do these policies violate G-R?
Each prefers route through neighbor (over direct)
Thus, if 0 is a peer to all them, then
  1 must be 2’s customer (since 2 prefers 2-1-0 over 2-0)
  2 must be 1’s customer (since 1 advertises route to 2))
Similar reasoning applies to any set of relationships between 0, 1, 2, 3

## Slide 61: Policy Oscillations (cont’d)
Policy autonomy vs network stability
  Policy oscillations with even small degree of autonomy
  Focus of much recent research
Not an easy problem
  PSPACE-complete to decide whether given policies will eventually converge!
However, if policies follow normal business practices, stability is guaranteed
  “Gao-Rexford conditions”

## Slide 62: Theoretical Results (in more detail)
If preferences obey Gao-Rexford, BGP is safe
  Safe = guaranteed to converge
If there is no “dispute wheel”, BGP is safe
  But converse is not true
If there are two “stable states”, BGP is unsafe
  But converse is not true

## Slide 63: (4) Performance Nonissues
Internal routing (non)
  Domains typically use “hot potato” routing
  Not always optimal, but economically expedient
Policy not about performance (non)
  So policy-chosen paths aren’t shortest
AS path length can be misleading (non)
  20% of paths inflated by at least 5 router hops
Notes: Lesson: not being optimal: who cares
Not being connected: we all care!!

## Slide 64: Performance (example)
AS path length can be misleading
  An AS may have many router-level hops
AS 4
AS 3
AS 2
AS 1
BGP says that
path 4 1 is better
than path 3 2 1

## Slide 65: Real Performance Issue: Slow convergence
BGP outages biggest source of Internet problems
Labovitz et al. SIGCOMM’97
    10% of routes available less than 95% of time
    Less than 35% of routes available 99.99% of the time
Labovitz et al. SIGCOMM 2000
    40% of path outages take 30+ minutes to repair
But most popular paths are very stable
Internet better if stability were a policy attribute
Notes: Lesson: not being optimal: who cares
Not being connected: we all care!!

## Slide 66: BGP Route Recalculation
Many more paths need to be recomputed in BGP
  Compared to DV
Why?
This is part of BGP’s slowness to respond
  Large routing table updates
  Need to suppress rapid changes
  Path exploration (updates every time a new path is tested, not just when the distance changes)

## Slide 67: (5) BGP Misconfigurations
BGP protocol is both bloated and underspecified
  lots of attributes
  lots of leeway in how to set and interpret attributes
  necessary to allow autonomy, diverse policies
  but also gives operators plenty of rope
Much of this configuration is manual and ad hoc
And the core abstraction is fundamentally flawed
  disjoint per-router configuration to effect AS-wide policy
  now strong industry interest in changing this! [later: SDN]
Notes: Lesson: not being optimal: who cares
Not being connected: we all care!!

## Slide 68: (6) World of Policies Changing
ISPs are now “eyeball” and/or “content” ISPs
Less focus on “transit”, more on nature of customers
No systematic policy practices yet
  Details of peering arrangements are private
And interconnection points (IXPs) are replacing many pairwise peering arrangements

## Slide 69: BGP: How did we get here?
BGP was designed for a different time
  before commercial ISPs and their needs
  before address aggregation
  before multi-homing
We don’t get a second chance: `clean slate’ designs virtually impossible to deploy
Thought experiment: how would you design a policy-driven interdomain routing solution?
1989 : BGP-1 [RFC 1105]
  Replacement for EGP (1984, RFC 904)
1990 : BGP-2 [RFC 1163]
1991 : BGP-3 [RFC 1267]
1995 : BGP-4 [RFC 1771]
  Support for Classless Interdomain Routing (CIDR)
Notes: Lesson: not being optimal: who cares
Not being connected: we all care!!