## Slide 1: CS 168 Current and Future Trends
Fall 2016
Scott Shenker
CS168.io
http://inst.eecs.berkeley.edu/~cs168/fa16/

## Slide 2
Ssssshhhhhhhhhhhhhhh

## Slide 3: Office Hours
Today: after class (in Soda 415)
Thursday: after class (in Soda 415)
These are your last chances to participate!
  Along with class today. Don’t count on Th lecture.
Reading week: review session in this classroom
  Day: T or Th (TBD)
  No prepared slides
  Submit questions by email beforehand

## Slide 4: Today: Current and Future Trends
New networks: Datacenters
  Other: 5G, IXPs
Deploying new functionality: Middleboxes, NFV
  Other: Low latency (Edge Computing)
New technology: Programmable forwarding chips
New Internet: Redesigning the Internet
  In 30 minutes!

## Slide 5: Datacenter Networks
New Networks

## Slide 6: What’s New: Topology
Servers clustered into racks
  ~40 servers per rack
Switches:
  Top-of-Rack
  Aggregation switches
Designed for full bisection bandwidth
  Nodes can communicate at full speed with each other

## Slide 7: E.g., “Fat Tree” Topology [Sigcomm’08]
Notes: Few things to notice:
3 stages (can think of as edge / aggregation / core)
All switches have same number of ports (=4) [hence k^3/4=16 end hosts]
All links have same speed
Many paths

## Slide 8: What’s new: Infrastructure
Scale ~1M servers/site [Microsoft/Amazon/Google]
  Expensive to build (~1B), must manage at scale
Complete control over entire design
  Can modify network and endpoint(s)
Very low RTTs within DC (measured in μsecs)
  BW x delay: 10Gbps x 1μsec = 10000 bits = 1250B
Implications for congestion control…
  New design regime, and freedom to implement

## Slide 9: What’s New: Applications
Customer-facing, revenue generating services
Large-scale computations (“big data”)
  Many internal request/response flows in map-reduce or similar computational frameworks
Responses to external requests must be fast
  Each external request spawns many parallel internal request/response interactions before external response
  Can return external response only when all internal interactions finish
Worst-case (“tail”) latency is critical
  Typical designs focus on average delay, here it is the tail

## Slide 10: What’s New: Usage Model
Multitenancy is common
  Certainly for Amazon’s EC2
  But even at Google and others
Requires sophisticated management
  To keep everything isolated
  To allocate to customers fairly
  …
Network virtualization (as in SDN) is key enabler

## Slide 11: What’s New in Datacenters
Topology (full bisection bandwidth)
Scale
Small BDP (new CC regime)
Complete local control (that enables new designs)
Applications (that make tail latency relevant)
Multitenancy (making Net. Virt. Crucial)

## Slide 12: Any Questions?

## Slide 13: Other New Networks
5G Wireless
  Promises everything to everyone
  High bandwidth, extremely low latency, etc….
  “Slicing” (can have several networks on same infra.)
Interconnection Points (IXPs)
  Usually interdomain connections are bilateral
  But IXPs are points where 100s or ASes interconnect
  May provide basis for evolving BGP…
    Because can make local changes....

## Slide 14: Middleboxes
Deploying New Functionality

## Slide 15: What is a middlebox?
  “…any intermediary device performing functions other than the normal, standard functions of an IP router on the datagram path between a source host and destination host.” [RFC 3234]

## Slide 16: Middleboxes Differ from Routers
Behavior: middleboxes implement more complex and diverse functionality
State: middleboxes can keep fine-grained state based on that packets it has processed.
  Such as hole-punching firewalls…
Notes: Buy a new middlebox, you need to learn what it does exactly. Routers can be hard to configure and have different CLI, but the basic functionality is the same! State: routers have a flow table that is updated through control plane, middleboxes keep state based on what it sees in the dataplane – can potentially be updated with every packet!

## Slide 17: Why Middleboxes?
Network architecture has not changed significantly for over forty years.
  Impossible to introduce new functionality architecturally
Middleboxes have become the de-facto way we implement and deploy “smarter” traffic processing in the network infrastructure.
  Just put boxes into network
  Don’t change any hosts/routers
Notes: Some work on middleboxes worked on how to avoid them, or even called them abominations, but the message from industry is strong: this is how we’re doing it, and they are here to stay!

## Slide 18: A Survey (Sherry et al.)
57 enterprise network administrators
Small (< 1k hosts) to XL ( >100k hosts)
Asked about deployment size, expenses, complexity, and failures.

## Slide 19: How many middleboxes do you deploy?
Typically on par with # routers and switches.

## Slide 20: What kinds of middleboxes do you deploy?
Many kinds of devices, all with different functions and management expertise required.
Notes: More devices == more expertise needed

## Slide 21: Variety of Middleboxes
Firewalls
NIDS
Media gateways
Load balancers
Proxies
VPN gateways
Voice gateways
WAN Optimizers

## Slide 22: Project 4: WAN Optimizer
Steve McCanne read the LBFS paper
Realized it would help companies
Now a many billion-dollar business
That you can duplicate in a few hours!

## Slide 23: History of Middlebox Deployment
Phase 1 of middleboxes:
  Deployed as dedicated box, custom HW
Phase 2 of middleboxes:
  Deployed as dedicated box, commodity HW
Phase 3 of middleboxes:
  Deployed as VM running on commodity rack
  This is the focus of much of our group’s research

## Slide 24: Network Function Virtualization
Basic approach:
  Deploy Network Functions (NFs) as VMs on racks
  Driven by carriers, for cost and complexity reduction
  Just spin up NFs as needed
  And specify traffic class to NF-chain mapping
Technical challenges:
  Speed (packets per second)
  Seamless scaling, failover, upgrades
  Ease of writing NFs
  …

## Slide 25: NFV Enables “Edge Computing”
NFV allows one to place NF functionality at edge
Offloads computation from
  End-devices (to lessen computation burden)
  Datacenters (to reduce latency)
Generalization of CDNs (e.g., Akamai)

## Slide 26: Any Questions?

## Slide 27: Programmable Forwarding Chips
New Technology

## Slide 28: Fixed Function vs Programmable
Previous forwarding chips had fixed functions
  Looked at fixed set of header fields
  Performed fixed set of functions based on those fields
New generation of chips allow for defining the parsing and control flow for packets with high-level language (P4)
  Set of functions are still fixed
  But can apply them much more flexibly
  Based on arbitrary parsing of packets

## Slide 29: “Classic” OpenFlow (1.x)
Target Switch
SDN Control Plane
Installing and querying rules

## Slide 30: “OpenFlow 2.0”
Target Switch
SDN Control Plane
Populating:
Installing and querying rules
Compiler
Configuring:
Parser, tables, and control flow
Parser & Table Configuration
Rule Translator
Notes: Two modes: (i) configuration and (ii) populating
Compiler configures the parser, lays out the tables (cognizant of switch resources and capabilities), and translates the rules to map to the hardware tables
The compiler could run directly on the switch (or at least some backend portion of the compiler would do so)

## Slide 31: Ideological Battle?
Will future networks be dominated by
  Programmable switches?
  Software edges?
In reality, you’ll probably have both
  Programmable switches come at little additional cost
    Enable monitoring in core
  But they cannot replace generality of software edge
    Can implement everything else…(e.g., middleboxes)

## Slide 32: Rearchitecting the Internet
This will be confusing. Ask questions!

## Slide 33: Problems with Today’s Architecture
“Accidents”
  Aspects widely used before seriously designed
  Or had to be redesigned under severe constraints
Oversights
  Issues that were never seriously considered
Open questions
  Issues that remain unanswered today….

## Slide 34: “Accidental” Aspects of Architecture
Addressing, multihoming, and aggregation
  Scaling relies on aligning allocation and topology
  No one would pretend CIDR is a fundamental design
    LPM is not just an optimization, but needed for correctness!
Naming
  Designed for scaling and autonomy, not authentication
Crucial aspects largely ignored by architecture
  Domains
  Middleboxes

## Slide 35: Implications of Middleboxes/Domains
Domains:
  Original network architecture: hosts/networks
  New network reality: hosts/networks/domains
  While addresses are broken into host/network components, there is no “domain” component”
Middleboxes:
  mboxes violate E2E principle
  But mboxes are right, and the E2E principle is wrong
  Wrong for functionality that is not host-oriented

## Slide 36: Oversights
Evolution: how do you change the architecture
  The version number in IP doesn’t address all the issues
DDoS: preventing denial-of-service attacks
  Nothing in today’s architecture helps with this

## Slide 37: A Big Open Question
Is packet delivery right interface for the Internet?
Some believe put-get is a better interface:
  Put: publish content, so others can retrieve
  Get: retrieve specified content (from nearest location)
  Information-centric networking (ICN)
    Interface is host-content, not host-host
Others advocate delay-tolerant networking (DTN)
  Make no assumption about ends both being up
  Put-get makes delay-tolerant networking easier
    Since there is no host-to-host interface

## Slide 38: Problems with Today’s Architecture
“Accidents”
  Addressing, naming, domains, middleboxes,…
Oversights
  Evolution, DDoS
Open questions
  What’s the right network interface?

## Slide 39: How I would address these problems
Step#1: Change naming
  Provide basis for authentication without certificates
Step#2: Change basic addressing
  Integrate domains into architecture
Step #3: Change how we build networks
  Making middleboxes part of the architecture
  Enable domains to support new protocols
Step #4: Solve the evolution problem
  Identify and avoid the barriers to evolution
  And let history decide what’s the right interface….

## Slide 40: Internet Naming: Take 2
Repeats past material….

## Slide 41: Use Self-Certifying Names
Names are of the form: P:L
  P: hash of public key associated with “owner” of object
    E.g., CNN, or Scott Shenker, or UC Berkeley
    P stands for “principal” or “provenance”
  L: label of object
    Latest headlines, or homepage, or class schedule
Each object consists of the following:
  Data
  Public key associated with principal for that object
  L
  Metadata
  Signature over all of the above

## Slide 42: Problems with this approach?
Scaling: names are “flat”
  But Google can resolve flat names at scale
Recall: how can I remember a 256-bit name?
  Names used by network not those exposed to humans
  People have private set of human-readable names
Key compromise: (or lack of uniqueness)
  Must register key (in Google-like database)
  When used for access, etc., usage is stored there
  Can negate a key if detect problem (cannot be undone)

## Slide 43: Any Questions?

## Slide 44: How I would address these problems
Step#1: Change naming
  Provide basis for authentication without certificates
Step#2: Change basic addressing
  Integrate domains into architecture
Step #3: Change how we build networks
  Making middleboxes part of the architecture
  Enable domains to support new protocols
Step #4: Solve the evolution problem
  Identify and avoid the barriers to evolution
  And let history decide what’s the right interface….

## Slide 45: Internet Addressing: Take 2
Repeats past material…

## Slide 46: New Addressing Architecture
Addresses are of the form: A:B:C:H
H is the name of the end host (or interface)
A, B, C, etc are routable “regions”
  Outermost address must be globally routable (domain)
  B must be routable within A
  C must be routable within B
All addresses are hashes of associated public key

## Slide 47: Forwarding
Basic correctness: A:B:C:H
  Route towards A
  Once inside A, route towards B
  …
Optimization:
  Can always look ahead to “deeper” match
  Still looking for exact matches, so easier than LPM
Note: LPM is harder and needed for correctness
  Deepest match is easier, and an optimization

## Slide 48: Interdomain Routing
Routes computed in terms of domains A
  Can then easily build BGP security into protocol
    Sign route advertisements
Host can belong to multiple domains
  A:H, B:H
  Interdomain routing need not worry about multihoming
  It just carries packets to specified domain
Doesn’t solve all conceptual problems with interdomain routing, but does clean it up…

## Slide 49: DDoS Prevention
DDoS attacks leverage compromised hosts
  Owners are benign, but host is compromised
Have NICs support “shut-off” packets (SOP)
  H1 can tell H2 to not send it any more packets
  Request is processed by the NIC
  Compromised OS can’t prevent enforcement
SOPs can be verified
  H1 can prove it sent the packet
  And can prove it has a packet from H2

## Slide 50: How SOPs Work
First-hop routers verify host addresses
  No spoofing possible
When host receives unwanted packet, it sends SOP
  Includes portion of unwanted packet
  Signs payload
Receiving NIC can verify:
  That it sent an unwanted packet
  That the SOP is from the recipient

## Slide 51: Paradigm Change
Internet service model is not just:
  Anyone can send a packet to anyone
It is now:
  Anyone can send a packet to anyone, unless the recipient expressly asks to not receive packets from sender
Enabled through use of self-certifying addresses
Cleaner than “capability-based” designs….

## Slide 52: Any Questions?

## Slide 53: How I would address these problems
Step#1: Change naming
  Provide basis for authentication without certificates
Step#2: Change basic addressing
  Integrate domains into architecture
Step #3: Change how we build networks
  Making middleboxes part of the architecture
  Enable domains to support new protocols
Step #4: Solve the evolution problem
  Identify and avoid the barriers to evolution
  And let history decide what’s the right interface….

## Slide 54: Network Infrastructure: Take 2

## Slide 55: Current Network (Domain) Design
Two main ingredients:
  HW switches/routers
  HW middleboxes
Only supports protocols designed into boxes
To deploy new middleboxes, must insert new HW
  CAPEX
  OPEX
Inflexible in both placement and protocols!

## Slide 56: New Approach: HW Core, SW Edge
Build domain core with traditional HW
  Handles forwarding (unicast, anycast, multicast) and TE
Build domain edge with SW (x86), handling all else:
  Isolation, access control, virtualization, …
  Middleboxes
  Use NFV-like approach to build
Domain has edge clusters and switched core:
  Clusters at edge run middleboxes in VMs (or equivalent)
  Core is based on HW switches/routers

## Slide 57: Flexibility
Middleboxes: just spin up a VM
Protocols:
  Support all internetwork (L3) protocols at edge
  Use an L2-like protocol for all internal forwarding
Supporting new L3 protocols via edge SW
  No internal changes needed!
  But do need changes to hosts (later in lecture)

## Slide 58: Paradigm Change
Build domains the way we build networks (subnets):
  External protocol is internetwork protocol
  Internal protocol is “private” protocol
    Could be IP, or IPv6, or whatever
No exposed internal addresses besides hosts H
  Host addresses H are location-independent
Domains have great:
  Flexibility: can implement new protocols/mboxes in SW
  Autonomy: can implement whatever they want internally

## Slide 59: Software vs Hardware
We are not claiming that software forwarding is as fast or cost effective as hardware forwarding
  2 orders of magnitude difference, perhaps growing?
We only claim that edge forwarding requirements can be met with software
  Estimates: large ISPs have ~10Tbps of edge bandwidth
  This entails $150,000 of infrastructure (for min-sized pkts)
  This barely pays for a single mid-range router
The HW vs SW debate isn’t over which is faster
  It is over whether HW is necessary at the edge
  And whether complex functionality is necessary in core

## Slide 60: Implications
Note that most network functionality driven by SW
SW comes in several kinds:
  Mbox code (at edge)
  SDN controller code (managing domain)
  Other packet processing at edge (new protocols)
None of it is tied to particular boxes
Network functionality will move at the speed of SW!
  Biggest change in networking since the Internet!

## Slide 61: Any Questions?

## Slide 62: How I would address these problems
Step#1: Change naming
  Provide basis for authentication without certificates
Step#2: Change basic addressing
  Integrate domains into architecture
Step #3: Change how we build networks
  Making middleboxes part of the architecture
  Enable domains to support new protocols
Step #4: Solve the evolution problem
  Identify and avoid the barriers to evolution
  And let history decide what’s the right interface….

## Slide 63: Evolution: Take 1

## Slide 64: Evolution: Changing the Architecture
Changing the architecture without “flag day” requires coexistence of architectures
Coexistence of new architectures is necessary and sufficient for evolution, so we focus on this
What would it take for multiple architectures to coexist?

## Slide 65: What’s Needed for Coexisting Archs?
Need to indicate which architecture you are using
  And retain backwards compatibility for those unaware of new architecture.
  This is called extensibility
There are some parts of the architecture that change very slowly (if at all)
  Must shield them from architectural change, while allowing them to benefit from their existence
  This is called modularity

## Slide 66: What Can Change, What Can’t
Can change relatively easily:
  Host OS, router software support, new applications
Difficult but possible to change:
  Deployment of new architectures in domain
  But much easier with new domain design….
Extremely hard to change: (architectural “anchors”)
  “Legacy” applications
  Anything the involves universal agreement (e.g., like current agreement on IP as narrow waist)
Notes: Change requiring first two: feasible
Requiring last: infeasible.

## Slide 67: The Design Question
You cannot evolve if you have to:
  Change legacy applications
  Get all domains to change over simultaneously
Can we evolve without changing the “anchors”?
This is key distinction between feasible and infeasible

## Slide 68: What About Current Architecture?
Internet architecture typically described in layers
But that picture ignores the “structure” of the Internet
Can look at the Internet a different way…

## Slide 69: A New Way of Looking at Architecture
Domain
Application
Network Stack
Rest of Internet (via BGP)
IP

## Slide 70: Basic Interfaces/Interactions
Network API (NetAPI)
  How application invokes network stack
  Legacy applications are one anchor
Interdomain protocol (or service model)
  How domain interacts with other domains
  Universal agreement on interdomain the other anchor

## Slide 71: Rigidity of Current Architecture
Domain
Application
Network Stack
Rest of Internet (via BGP)
IP

## Slide 72: The Role of IP
Many (old) apps are aware of IP
IP is also how you interact with other domains
  Basis of interdomain routing
Neither of these are relevant to IP’s original goal, routing between subnetworks.

## Slide 73: Rigidity of Current Architecture
Domain
Application
Network Stack
Rest of Internet (via BGP)
IP
Current architecture is worst case for evolution, with IP embedded in both anchors

## Slide 74: Any Questions?

## Slide 75: Back to Design Question
Can we evolve without changing the “anchors”?

## Slide 76: The Answer is Yes!
Make network API (netAPI)
  Extensible (allow apps/stacks to choose functionality)
  Modular (only expose necessary semantics)
Remove need for universal agreement on single interdomain service model, by making interdomain interface:
  Extensible (allow apps/stacks to choose functionality)
  Modular (only expose necessary semantics)

## Slide 77: The New Internet
Domain
Application
Network Stack
Rest of Internet
ISMs
netAPI
Network stack and domain have complete freedom to innovate
Notes: Mention IPv6 as in network stack/domain: seamless….

## Slide 78: Design of Network API
Modular: keep networking details out of interface
  Let stack resolve names, understand network details, etc.
Extensible: put “schema” identifier in netAPI
  Schemas represent different API styles
  Updated applications can invoke new functionality

## Slide 79: Example Schemas
Schema ID | Primitives | Data Structure
Sockets | open, connect, accept, read, write, close | Bytes
Publish/Subscribe | publish, subscribe | Publications
RPC | send_request receive_request | Function call and response
Multimedia | play | Audio/video frames
… | … | …
Only standardizing Schema ID
the way applications specify their choice of schema
(a trivial level of indirection)

## Slide 80: How Are These Schemas Supported?
Some can be supported by end host
  RPC-like schema merely moves functionality into stack
But others “require” network support
  E.g., Information-centric network (ICN) designs “require” network to support put/get interface
New Interdomain service models (ISMs)
  Agreement between some domains on new network functionality

## Slide 81: Interdomain Service Models (ISMs)
Methods of communicating across domains
  Ucast/mcast/acast packet delivery
  Delay-tolerant networks
  ICN (e.g., DONA, NDN, etc.)
ISMs handle all interdomain issues
  Domain addressing, routing (if applicable)
  DoS, congestion control, etc.
ISMs do not dictate intradomain design
  The implementation of an ISM might affect domain design
  But definition of an ISM does not dictate domain design

## Slide 82: Design Principles
Extensible:
  “Packets” carry ISM identifier telling domain how to handle
  Thus, can have many ISMs running in parallel
Modular:
  Host only aware of syntax and semantics of ISM “header”
  Does not need to be aware of ISM implementation

## Slide 83: Partial Deployment and Compatibility
If an entity’s domain hasn’t implemented ISM then:
  Sender gets “unreachable” message, tries another ISM
  Or host can “join” ISM by tunneling through to ISM node
For two hosts to communicate, they:
  Must use compatible host-level protocols (transport, etc.)
  Must be connected by at least one ISM path
    ISM reachability may be visible (depends on ISM)
Notes: Applies to content-oriented ISMs as well (in terms of unreachable)

## Slide 84: Provides Framework For Evolution
Only standardize syntax for specifying ISM, Schema
  No need for global agreement on anything more
Clean separation btwn domain internals and ISMs
  Domains can use any internal technology to support ISMs
  Can choose what ISMs to support
Clean separation btwn applications and network
  Network can evolve without application’s knowledge
Claim: this is enough to make innovation feasible
  Can be implemented in a backwards compatible fashion

## Slide 85: Huh?
Can think of this as making everything within a domain an L2-like protocol
  No need for agreement on L2 technologies
ISMs can be deployed in parallel
  Can be supported by subset of domains (tunneling)
  Global agreement not necessary
ISMs handle interdomain addressing
  Domains can adopt their own intradomain addressing
  This is where IP failed!

## Slide 86: Don’t We Need a Narrow Waist?
Each ISM needs a narrow waist
  The waist is what all participating domains agree on
But there can be more than one such waist
The fact that we thought we needed only one waist is because we use IP for both interdomain and intradomain communication
  Cerf/Kahn got this right (when domains were networks)
  We messed this up when domains and networks diverged

## Slide 87: Summary
What was once seen as a tautological impossibility
  Architecture is what we all agree on
  How can we possibly change it without a flag day
Can be seen as almost inevitable consequence of good design practice
  Modularity
  Extensibility

## Slide 88: Scorecard of Problems
Aggregation/Multihoming/Domains: solved
DDoS: solved
Middleboxes: solved
Evolution: solved
Future network interface: let history decide….
  No reason to choose a single one now...

## Slide 89: We are done….
One more lecture to go!